## Slide 1: Definitions
y (up)
z (West)
x (South)
n,b
t,g
d,a
STAR Global Coordinates
Wafer Local Coordinates
w (normal/away from ladder)
v (along ladder +z)
u (r-phi direction for RHS)
n,β
t, g
d,a
Local v (along ladder) is fixed and along global +z
Local w (normal to u-v [wafer] plane). Points away from exposed surface
Local u (r-phi on wafer plane) varies so it forms a RHS with v-w (u,w,v)
Alignment Details
S. Margetis, KSU

## Slide 2
Wafer Local Coordinates Details
v (along ladder +z)
u (r-phi direction for RHS)
n,β
t, g
d,a
w (normal/away from ladder)
We use the above RHS notation (u,w,v)
Karimaki et al (CMS) use the (u,v,w) notation. In that system v=- (our v) otherwise system is left-handed
So the documentation is confusing…needs some straightening up….
A
B
Gene Van Buren et al.

## Slide 3
Wafer Local Coordinates Details
v (+z)
u (r-phi)
n,β
t, g
d,a
w (normal)
x = xd = u => dx = dxd = du
y = xn = w => dy = dxn = dw
z = xt = -v => dz = dxt = dv
a = fd = a => sina = dfd = da
b = fn = g => sinb = dfn = dg
g = ft = -b => sing = dft = -db
Gene Van Buren et al.
v (-z)
u (r-phi)
n,g
t, b
d,a
w (normal)
Karimaki -CMS

## Slide 4
Wafer Local Coordinates Details
Uses correct correction = du = vprediction - vhit
track-plane angles use a,b,g convention for sign
udn =- tanf
utn=tanθ
A
B
v (along ladder +z)
u (r-phi direction for RHS)
n,β
t, g
d,a
w (normal/away from ladder)
Gene Van Buren et al.
tanf<0
v (along ladder +z)
u (r-phi direction for RHS)
n,β
t, g
d,a
w (normal/away from ladder)
udn=ud/un>0
Uses vhit-vprediction so it needs a (-) sign
track-plane angles sign comes from component
udn =- tanf
utn=tanθ
tanq>0
utn=ut/un>0
See next page for more details

## Slide 5
…which after the convention corrections reach agreement with the exception of Chakraborty that has a sign problem [must be a typo]
Need to reconcile this sign – most likely a typo
My Math shows others to be right

## Slide 6
Local PXL system definitions (offline)
w (away)
v (West)
u (across)
w
v
u
sensor
ladder
PXL Sector origin is the same as STAR global
  use same convention as in SSD/IST (as a whole) and IDS to simplify software
EAST
WEST

## Slide 7
u
u

## Slide 8: Offline use of Geometry Info
Local-to-Global transforms are done in terms of TGeoHMatrix
This can be e.g. the center of a sensor or a pixel.
d,n,t are unit vectors and a, b,g the corresponding rotation angles in x,y,z [u,w,v] directions [RHS] . dx is the unit vector d projection on the x-axis etc
TGeoHMatrix definition
Local to Global transformation - definition

## Slide 9
For small rotations [8]
Successive small rotations are additive, group Abelian(!) [a2=b2=g2=ab=…=0]
That is why we use multiplications to move from one system to another
PG = Tpc2Global *GL * PI *DP * SD * WLL;
PXLInGlobal=Tpc2Magnet*IDS2Tpc*PXL2IDS*DShell2PXL*Sector2DShell*(Pxl-Sector)

## Slide 10
Example: PXL Sector-4 Ladder-1 and 2
d
n
X
Y
n
d

## Slide 11
SECTOR 2
____________________________________________________________________________________________________
|dX mkm |dY mkm |dZ mkm |alpha mrad |beta mrad | gamma mrad |Comment
______________________________________________________________________________________________
| -250 | -200 | 0 | 5 | -5 | 0 | PXL sector 2 Ladder 1
______________________________________________________________________________________________
| -500 | -250 | -380 | 5 | -5 | 0 | PXL sector 2 Ladder 2
______________________________________________________________________________________________
| -200 | -200 | 0 | 5 | -5 | 0 | PXL sector 2 Ladder 3
______________________________________________________________________________________________
| -170 | -200 | -500 | 5 | -5 | 0 | PXL sector2 Ladder 4
______________________________________________________________________________________________
SECTOR 4
______________________________________________________________________________________________
80 | -300 | -300 | 1 | 1 | 0 | PXL sector 4 Ladder 1
_____________________________________________________________________________________________
| -30 | 150 | -300 | 1 | 1 | 0 | Ladder 2
______________________________________________________________________________________________
| -80 | 220 | -420 | 1 | 1 | 0 | Ladder 3
________________________________________________________________________________________________
| -200 | 300 | -400 | 1 | 1 | 0 | Ladder 4
Survey geometry + Calibrations: Based on day 155 from Long, got it 7/5
FIRST PASS ESTIMATED Corrections

## Slide 12
SECTOR 7
______________________________________________________________________________________________
-430 | -280 | 50 | -10 | 10 | 10 | PXL sector 7 Ladder 1
_____________________________________________________________________________________________
-800 | -350 | 350 | -10 | 10 | 10 | Ladder 2
________________________________________________________________________________________________
-450 | -350 | 200 | -10 | 10 | 10 | Ladder 3
________________________________________________________________________________________________
-200 | -250 | 50 | -10. | 10 | 10 | Ladder 4
Survey geometry + Calibrations: Based on day 155 from Long, got it 7/5
FIRST PASS ESTIMATED Corrections

## Slide 13
Local to Global
Inverse turns out to be just the transpose of the original matrix
Global to Local

## Slide 14
Example: small rotation only in Global system around z-axis, dg (da=db=0)
ΝOTE: All transformations are Local-to-Master type:
y (up)
z (West)
x (South)
n
t
d
+dg
x,y,z=X,Y,Z
x’,y’,z’
.
.
u,v=A,B
u’,v’=A,B
Global system

## Slide 15: Backup -1

## Slide 16
Example: small rotation only in Global system around z-axis, dg (da=db=0)
ΝOTE: All transformations are Local-to-Master type:
y (up)
z (West)
x (South)
n
t
d
+dg
x,y,z=X,Y,Z
x’,y’,z’
.
.
u,v=A,B
u’,v’
Global system
In Local system the same appears as rotation by dg plus a translation by Dr=(r’-r)

## Slide 17
Offline Structures
PG = Tpc2Global *GL * PI *DP * SD * WLL;
PXLInGlobal=Tpc2Magnet*IDS2Tpc*PXL2IDS*DShell2PXL*Sector2DShell*(Pxl-Sector)
HFT PXL
Fixed for all HFT detectors
Fixed for PXL by Offline
Fixed by PXL SURVEY

## Slide 18
Offline Structures
PG = Tpc2Global *GL * PI *DP * SD * WLL;
PXLInGlobal=Tpc2Magnet*IDS2Tpc*PXL2IDS*DShell2PXL*Sector2DShell*(Pxl-Sector)
HFT PXL
WLL = LS * SL * PS (TPS fn);
PXLInSector=Ladder2Sector*Sensor2Ladder*Pxl2Sensor
HFT PXL
Survey Structures

## Slide 19: Assumptions
Survey and Offline systems will differ. Data formats will differ too. Transform from one system to other possible.
Origin of coordinate systems should be as close as possible to geometrical center of the module -> minimize effects
  easy to work also with GEANT volume-placing matrices
  unless there is a clear reason for not doing this
Sensor center is center of active area
Ladder center in-between sensors 5-6 (geometrical center)
Sector center (proposed) to be the innermost (ladder #4) center due to the importance of first layer, rotated 180 by necessity (see next slide)
TPS fits are assumed to be done on single sensor basis
  pixel functions/parameters will be tagged with sensor ID

## Slide 20: HFT Alignment Procedures
S. Margetis, KSU
Introduction
HFT Configuration – System hierarchy
(thoughts on) Proposed procedures
Tools/Implementation (Jonathan)
Plans, Timeline and Issues
Summary
Alignment procedures review, BNL, Oct. 12, 2012

## Slide 21
Flowchart of Geometry/Survey/Alignment
Sensor/Ladder Survey
Save – CVS?
Fit, get structures
Save – Db
GEANT geometry
Apply*
RawData
Apply
Alignment
Correct
Done
N
Y
Update – Db
HITS
Final Reco Pass
ForEachRun
ForEachNewSector/Ladder
Mis-align/Check Alignment software
* VMC, STV ready

## Slide 22: Introduction
Anything we build or touch or use needs Modeling, Survey and in-situ Alignment
  i.e. versioning
Survey will freeze position of sensors on sectors (PXL). Help also with sector on hemisphere (PXL?). For SSD/IST will freeze position of sensors on ladder and ladder shape
For each yearly Run the in-situ position of major detector elements needs to be rechecked

## Slide 23: Reference System Hierarchy
STAR Magnet=STAR system
TPC system
Fixed x,y,z
Fixed-1D-rot
Float
Star Magnet defines overall system (Field map)
TPC is the first important system for HFT (relative positioning), attached to Magnet

## Slide 24
IDS/MSC
ESC/WSC attached to TPC wheel. It defines the HFT system’s relation (as a whole) to TPC system
See next slides for systems inside the HFT complex

## Slide 25
25
PST (IST)
OSC (SSD)

## Slide 26: General Layout
IST
IST
SSD

## Slide 27: Reference systems - comments
In general survey accuracy of critical components (relative pixel and/or sensor positions) expected to be better than acceptable values
Will soon need surveyed positions of IDS targets
  to build ‘ideal’ position Db
  Sub-millimeter accuracies acceptable -> Tracks will fix them
All this information is represented as matrices (position/orientation) of their center-of-gravity. These matrices are used to define Local to Global transforms
GEANT geometry can/should be synchronized with Realistic Volume hierarchy instead of the current ‘patch-the-hit’ scheme
  - VMC environment will facilitate this

## Slide 28
WG = Tpc2Global * GL * SG * LS * WLL;
WaferInGlobal=Tpc2Magnet *SsdinTpc*SectorInSSD*LadderInSector*WaferInLadder
Local <-> Global transforms
WG = Tpc2Global * GL * LO * WLL;
WaferInGlobal=Tpc2Magnet *IDS2Tpc*Ladder2IDS*WaferInLadder
WG = Tpc2Global * GL * PI *LO * WLL;
WaferInGlobal=Tpc2Magnet *IDS2Tpc*PST2IDS*Ladder2PST*WaferInLadder
PG = Tpc2Global *GL * PI *DP * SD * WLL;
PXLInGlobal=Tpc2Magnet*IDS2Tpc*PXL2IDS*DShell2PXL*Sector2DShell*(Pxl-Sector)
OLD SSD
HFT SSD
HFT IST
HFT PXL

## Slide 29: Alignment methods (outline only)
There are ‘Global’ and ‘Self’ Alignment methods
  Global uses mostly ‘external’ track information
  Self uses mostly ‘internal’ track information
  For HFT we propose a mix (more Self !)
We have successful ‘Global’ methods already in place (SVT/SSD)
  TPC distortions, t0, ‘track tof’ etc is a problem
In HFT system we have significant sensor overlap to make use of ‘Self’ alignment methods. We also have high precision PXL info with excellent sector rigidity, survey info, placement.
We need to use this advantage
We lack a hardware monitoring system. Once detectors are installed we rely on survey and alignment software

## Slide 30
D.Chakraborty, J.D.Hobbs, D0 note Oct.13, 1999

## Slide 31
The sequence to be followed for each detector is:
1) SSD Alignment: (TPC tracks Only)
Global - SSD on Global and Sectors on Global;
Local - SSD Ladders on Sectors;
2) SVT Alignment: (TPC+SSD hits on tracks)
Global - SVT on Global and Shells on Global;
Local - SVT Ladders on Shells; (Drift Velocities);
3) Consistency Check: (TPC+SSD+SVT hits on tracks)
Global;Local (ladders);Drift Velocities;
SSD/SVT procedure (old)

## Slide 32
For alignment we use “good” (well defined) tracks fitted with the primary vertex. (e.g. NFP, pt cuts)
  Use of primary tracks significantly improves precision of track predictions in HFT and reduces influence of systematics.
  Good statistics is a must (up to a point)(see example in Jonathan’s talk)(50-100K hits per wafer/sensor)
In order to minimize TPC space-charge distortions, tracking errors (mismatches) and PXL pileup we will need to use low luminosity and low-medium multiplicity data as the alignment sample
Method is iterative since it is precise for small deviations
Notes: Heavy d

## Slide 33: HFT Proposed Procedure:
Remember: PXL detector is a big asset (c.f. TPC )
Global Alignment of PXL
  Relative alignment of PXL sectors and halves using overlap region AND halves using Event vertex found by each half
  Relative alignment of PXL and TPC [TPC primary tracks]
    Iterative->(PXL, PXL half, sector)
  Exact sequence/interplay needs to be determined
Primary tracks with TPC+PXL hits
  Alignment of IST ladders with respect to PXL
Primary tracks with (All – SSD) hits
  Alignment of SSD ladders
Check
We assume that sensors on ladder and ladders on sectors are pre-surveyed to specs

## Slide 34: Precision requirements for HFT alignment
Pointing accuracy is ultimate figure of merit: DCA resolution (in bending XY r plane: DCA), and resolution in non-bending plane: z
  2DCA= 2vertex+ 2track + 2MCS (the same for non-bending plane)
  primary vertex resolution: vertex ~ 3mm+(120 mm / √Nch); for central Au+Au collisions turns out to be ~5 mm
  track pointing resolution: track ~ 1.5 XY [in our case, where XY is intrinsic detector precision (~10mm)]  alignment errors
  multiple scattering (MCS): MCS ~ 20mm / bp (GeV/c) (for thin PXL)
Overall mis-alignments of < 10 mm or <MCS are acceptable
Notes: Heavy d

## Slide 35: DCA resolution
Number of Silicon Points fitted to track | XY @1GeV/c (m)
0 -  TPC only | 3350
1 -  TPC+SSD | 967
2 -  TPC+SSD+SVT | 383
3 -  TPC+SSD+SVT | 296
4 -  TPC+SSD+SVT | 281
SVT/SSD example
With increasing no. of fitted Si points it is improved by ~ order of magnitude.
Contribution from tracking (constant term) is comparable with MCS @ 1 GeV/c
XY

## Slide 36: Tasks
Need to finalize the PXL sensor representation in Db (prototype sector)
Need to setup Data formats, code to deliver matrices etc
Need to know/map the (realistic) error of every survey step
Need to start simulations to determine alignment software performance
Need to rework GEANT geometry synchronization (STV, VMC)
Need to finalize SSD procedures and initialize/define IST ones
Need to include gravitational sagging in SSD and IST (?) model
Need to keep/use expertise around

## Slide 37: Plans/Timeline
Some of these efforts need to go in parallel
It will take about a month or two to setup the chain and clean up the code for all HFT subsystems (current environment)
  Includes software, Db structures, Hit, conventions
We can do (some) tests in current environment or begin porting to VMC (with help)
By the end of the year we would need to have defined and have established working interfaces to Survey for PXL
Full chain ready to work with cosmics/data when available
Only then, when done, we can start looking at other packages

## Slide 38: Summary
The building up of a working chain is coming along
All 3 needed efforts are moving along (Geo, Sur, Al)
Benefited enormously from previous experience as we hope to benefit from current experience
A lot still needs to be done
Target to have a working chain for data beginning of the year is not unrealistic

## Slide 39: Backup-2

## Slide 40: References
“The STAR time projection chamber a unique tool for studying high multiplicity events at RHIC”, M.Anderson et al., NIM A499: 652,2003.
“The laser system for the STAR time projection chamber”, J. Abele et al., NIM A499: 692,2003.
“Correcting for distortions due to ionization in the STAR TPC”, G. Van Buren et al.,NIM A566:22-25,2006.
“The STAR Silicon Vertex Tracker” A large area Silicon Drift Detector”, R.Bellwied et Al., NIM A499: 640, 2003.
“The STAR silicon strip-detector (SSD)”, L.Arnold et al., NIM 2003 A499: 652, 2003.
“Alignment Strategy for the SMT Barrel Detectors”, D.Chakborty, J.D.Hobbs, October 13, 1999. D0 Note (unpublished)
“Sensor Alignment by Tracks”, V.Karimaki et al.,CMS CR-2004/009 (presented at CHEP 2003)
http://phys.kent.edu/~margetis/STAR/HFT/Survey/SVTSmallScaleSelfAlignment.pdf
http://phys.kent.edu/~margetis/STAR/HFT/Survey/SVT_Alignment_JPCSL.pdf

## Slide 41
D.Chakraborty, J.D.Hobbs, D0 note Oct.13, 1999

## Slide 42
http://drupal.star.bnl.gov/STAR/comp/calib/svt/selfalign