## Slide 1: HFT Alignment Procedures
S. Margetis, KSU
Introduction
HFT Configuration – System hierarchy
(thoughts on) Proposed procedures
Tools/Implementation (Jonathan)
Plans, Timeline and Issues
Summary
Alignment procedures review, BNL, Oct. 12, 2012

## Slide 2
Flowchart of Geometry/Survey/Alignment
Sensor/Ladder Survey
Save – CVS?
Fit, get structures
Save – Db
GEANT geometry
Apply*
RawData
Apply
Alignment
Correct
Done
N
Y
Update – Db
HITS
Final Reco Pass
ForEachRun
ForEachNewSector/Ladder
Mis-align/Check Alignment software
* VMC, STV ready

## Slide 3: Introduction
Anything we build or touch or use needs Modeling, Survey and in-situ Alignment
  i.e. versioning
Survey will freeze position of sensors on sectors (PXL). Help also with sector on hemisphere (PXL?). For SSD/IST will freeze position of sensors on ladder and ladder shape
For each yearly Run the in-situ position of major detector elements needs to be rechecked

## Slide 4: Reference System Hierarchy
STAR Magnet=STAR system
TPC system
Fixed x,y,z
Fixed-1D-rot
Float
Star Magnet defines overall system (Field map)
TPC is the first important system for HFT (relative positioning), attached to Magnet

## Slide 5
IDS/MSC
ESC/WSC attached to TPC wheel. It defines the HFT system’s relation (as a whole) to TPC system
See next slides for systems inside the HFT complex

## Slide 6
6
PST (IST)
OSC (SSD)

## Slide 7: General Layout
IST
IST
SSD

## Slide 8: Reference systems - comments
In general survey accuracy of critical components (relative pixel and/or sensor positions) expected to be better than acceptable values
Will soon need surveyed positions of IDS targets
  to build ‘ideal’ position Db
  Sub-millimeter accuracies acceptable -> Tracks will fix them
All this information is represented as matrices (position/orientation) of their center-of-gravity. These matrices are used to define Local to Global transforms
GEANT geometry can/should be synchronized with Realistic Volume hierarchy instead of the current ‘patch-the-hit’ scheme
  - VMC environment will facilitate this

## Slide 9: Definitions
y (up)
z (West)
x (South)
n,b
t,g
d,a
Global Coordinates
Local Coordinates
w (normal to ladder)
v (along ladder)
u (rphi)
t,g
n,b
d,a
Local v (along ladder) is fixed and along global z
Local w (normal to wafer plane) is fixed (points away from the interaction point
Local u (rphi on wafer plane) varies so it forms a RHS with v-ww

## Slide 10: Offline use of Geometry Info
Local-to-Global transforms are done in terms of TGeoHMatrix
This can be e.g. the center of a sensor or a pixel.
n,d,t are unit vectors and b,a,g the corresponding rotation angles, RHS
TGeoHMatrix definition
Transform example

## Slide 11
WG = Tpc2Global * GL * SG * LS * WLL;
WaferInGlobal=Tpc2Magnet *SsdinTpc*SectorInSSD*LadderInSector*WaferInLadder
Local <-> Global transforms
WG = Tpc2Global * GL * LO * WLL;
WaferInGlobal=Tpc2Magnet *IDS2Tpc*Ladder2IDS*WaferInLadder
WG = Tpc2Global * GL * PI *LO * WLL;
WaferInGlobal=Tpc2Magnet *IDS2Tpc*PST2IDS*Ladder2PST*WaferInLadder
PG = Tpc2Global *GL * PI *DP * SD * WLL;
PXLInGlobal=Tpc2Magnet*IDS2Tpc*PXL2IDS*DShell2PXL*Sector2DShell*(Pxl-Sector)
OLD SSD
HFT SSD
HFT IST
HFT PXL

## Slide 12: Alignment methods (outline only)
There are ‘Global’ and ‘Self’ Alignment methods
  Global uses mostly ‘external’ track information
  Self uses mostly ‘internal’ track information
  For HFT we propose a mix (more Self !)
We have successful ‘Global’ methods already in place (SVT/SSD)
  TPC distortions, t0, ‘track tof’ etc is a problem
In HFT system we have significant sensor overlap to make use of ‘Self’ alignment methods. We also have high precision PXL info with excellent sector rigidity, survey info, placement.
We need to use this advantage
We lack a hardware monitoring system. Once detectors are installed we rely on survey and alignment software

## Slide 13
D.Chakraborty, J.D.Hobbs, D0 note Oct.13, 1999

## Slide 14
The sequence to be followed for each detector is:
1) SSD Alignment: (TPC tracks Only)
Global - SSD on Global and Sectors on Global;
Local - SSD Ladders on Sectors;
2) SVT Alignment: (TPC+SSD hits on tracks)
Global - SVT on Global and Shells on Global;
Local - SVT Ladders on Shells; (Drift Velocities);
3) Consistency Check: (TPC+SSD+SVT hits on tracks)
Global;Local (ladders);Drift Velocities;
SSD/SVT procedure (old)

## Slide 15
For alignment we use “good” (well defined) tracks fitted with the primary vertex. (e.g. NFP, pt cuts)
  Use of primary tracks significantly improves precision of track predictions in HFT and reduces influence of systematics.
  Good statistics is a must (up to a point)(see example in Jonathan’s talk)(50-100K hits per wafer/sensor)
In order to minimize TPC space-charge distortions, tracking errors (mismatches) and PXL pileup we will need to use low luminosity and low-medium multiplicity data as the alignment sample
Method is iterative since it is precise for small deviations
Notes: Heavy d

## Slide 16: HFT Proposed Procedure:
Remember: PXL detector is a big asset (c.f. TPC )
Global Alignment of PXL
  Relative alignment of PXL sectors and halves using overlap region AND halves using Event vertex found by each half
  Relative alignment of PXL and TPC [TPC primary tracks]
    Iterative->(PXL, PXL half, sector)
  Exact sequence/interplay needs to be determined
Primary tracks with TPC+PXL hits
  Alignment of IST ladders with respect to PXL
Primary tracks with (All – SSD) hits
  Alignment of SSD ladders
Check
We assume that sensors on ladder and ladders on sectors are pre-surveyed to specs

## Slide 17: Precision requirements for HFT alignment
Pointing accuracy is ultimate figure of merit: DCA resolution (in bending XY r plane: DCA), and resolution in non-bending plane: z
  2DCA= 2vertex+ 2track + 2MCS (the same for non-bending plane)
  primary vertex resolution: vertex ~ 3mm+(120 mm / √Nch); for central Au+Au collisions turns out to be ~5 mm
  track pointing resolution: track ~ 1.5 XY [in our case, where XY is intrinsic detector precision (~10mm)]  alignment errors
  multiple scattering (MCS): MCS ~ 20mm / bp (GeV/c) (for thin PXL)
Overall mis-alignments of < 10 mm or <MCS are acceptable
Notes: Heavy d

## Slide 18: DCA resolution
Number of Silicon Points fitted to track | XY @1GeV/c (m)
0 -  TPC only | 3350
1 -  TPC+SSD | 967
2 -  TPC+SSD+SVT | 383
3 -  TPC+SSD+SVT | 296
4 -  TPC+SSD+SVT | 281
SVT/SSD example
With increasing no. of fitted Si points it is improved by ~ order of magnitude.
Contribution from tracking (constant term) is comparable with MCS @ 1 GeV/c
XY

## Slide 19: Tasks
Need to finalize the PXL sensor representation in Db (prototype sector)
Need to setup Data formats, code to deliver matrices etc
Need to know/map the (realistic) error of every survey step
Need to start simulations to determine alignment software performance
Need to rework GEANT geometry synchronization (STV, VMC)
Need to finalize SSD procedures and initialize/define IST ones
Need to include gravitational sagging in SSD and IST (?) model
Need to keep/use expertise around

## Slide 20: Plans/Timeline
Some of these efforts need to go in parallel
It will take about a month or two to setup the chain and clean up the code for all HFT subsystems (current environment)
  Includes software, Db structures, Hit, conventions
We can do (some) tests in current environment or begin porting to VMC (with help)
By the end of the year we would need to have defined and have established working interfaces to Survey for PXL
Full chain ready to work with cosmics/data when available
Only then, when done, we can start looking at other packages

## Slide 21: Summary
The building up of a working chain is coming along
All 3 needed efforts are moving along (Geo, Sur, Al)
Benefited enormously from previous experience as we hope to benefit from current experience
A lot still needs to be done
Target to have a working chain for data beginning of the year is not unrealistic

## Slide 22: Backup

## Slide 23: References
“The STAR time projection chamber a unique tool for studying high multiplicity events at RHIC”, M.Anderson et al., NIM A499: 652,2003.
“The laser system for the STAR time projection chamber”, J. Abele et al., NIM A499: 692,2003.
“Correcting for distortions due to ionization in the STAR TPC”, G. Van Buren et al.,NIM A566:22-25,2006.
“The STAR Silicon Vertex Tracker” A large area Silicon Drift Detector”, R.Bellwied et Al., NIM A499: 640, 2003.
“The STAR silicon strip-detector (SSD)”, L.Arnold et al., NIM 2003 A499: 652, 2003.
“Alignment Strategy for the SMT Barrel Detectors”, D.Chakborty, J.D.Hobbs, October 13, 1999. D0 Note (unpublished)
“Sensor Alignment by Tracks”, V.Karimaki et al.,CMS CR-2004/009 (presented at CHEP 2003)
http://phys.kent.edu/~margetis/STAR/HFT/Survey/SVTSmallScaleSelfAlignment.pdf
http://phys.kent.edu/~margetis/STAR/HFT/Survey/SVT_Alignment_JPCSL.pdf

## Slide 24
http://drupal.star.bnl.gov/STAR/comp/calib/svt/selfalign

## Slide 25
D.Chakraborty, J.D.Hobbs, D0 note Oct.13, 1999