## Slide 1: HFT & PXL geometry
F.Videbæk
Brookhaven National Laboratory

## Slide 2: Overview
Inner Detector Support (IDS)
  Layout, nomenclature
PXL
  Sector description
  Ladder description
  Generation of geometry and material information
Summary

## Slide 3: Exploded view of the HFT inside the TPC
TPC Volume
Magnet
Return Iron
Solenoid
OFC
Outer Field Cage
IFC
Inner Field Cage
SSD
IST
PXL
EAST
WEST
FGT
HFT

## Slide 4: Support Structure Overview

## Slide 5: Pixel support structure near the vertex
2.5 cm radius
8 cm radius
Inner layer
Outer layer
End view
Carbon fiber support beams (green)
Two “D” sectors form the heart of the PXL detector. The two halves separate in order to allow for easy access, removal and repair.

## Slide 6: Physical Reality

## Slide 7: PXL Sector
Got all information from Howard Wieman how the layout was defined in SolidWorks (SW).
Shown in subsequent slides (which I will go got through in details
Checked with SW model. Extracted other info from there.
Put this information into a root script that generates cross section of geometry based on these rather complicated algorithms.
This method allows to repeat once the final sectors , and ladders are produced.

## Slide 8
sector geometry based on ladder layout ph1.SLDPRT (Sketch2)
The outer ladder positions are defined by placing the active edge of the pixel array (side opposite pad row) on an 80 mm radius and positioned 12 deg apart. The starting point for the first active region is placed 0.7885 mm from the vertical surface of the sector beam along the surface line of the active silicon.
The side surfaces of the sector beams are defined by lines 1 mm inside and parallel to the vertical radial line and the 36 deg radial line.
The ladder angle is defined by requiring a 1 mm overlap of the active regions for the phase 1 detector

## Slide 9
The grey rectangles have the length of the active region of phase 1 detector and the thickness represents what was expected to be the ladder thickness. This is what is used to define the sector beam surface that the ladder gets bonded to. The ladder thickness ended up slightly different than the value here of 0.7716 mm, so the ladders will be off a little from the 80 mm radius circle.
sector geometry based on ladder layout ph1.SLDPRT (Sketch2)

## Slide 10
sector geometry based on ladder layout ph1.SLDPRT (Sketch2)
The inner ladder is positioned with the active edge next to the wire pads on a 25 mm radius circle. The angle is defined by a 1 mm overlap of the active region. There is an arbitrary offset from the sector beam side edge.

## Slide 11: PXL ladder
For realistic simulation it is essential to get the proper layout of ladders.
Starting point
  Material budget from Leo
  SW model

## Slide 12: Ladder layout
Si-layer with inactive frames
Al-Kapton Cable
Carbon backing
Layers of adhesive

## Slide 13
Si 2 mil (0.0529%)
acrylic 2 mil (0.0148%)
sensor
cable
backer
support
beam
acrylic 2 mil (0.0148%)
acrylic 2 mil (0.0148%)
Al 0.7 mil (0.0124%)
kapton 1mil (0.0073%)
Al 0.7 mil (0.0124%)
Al 0.7 mil (0.0124%)
kapton 1mil (0.0073%)
Al 0.7 mil (0.0124%)
10 mil carbon composite
open weave (0.0587%)
4 mil silicon adhesive
(0.0469%)
9.6 mil carbon composite
sector beam (0.1017%)
0.0677%
0.079%
0.223 mm
0.2221%
TOTAL = 0.3688 % X0
Notes: Curtsey Leo

## Slide 14: Ladder Cable and Si
Note that cable layout is slightly different 2 layer Al with total 0.073%.
Implemented Cable & Si component in my scripts
Materials for this have proper Radiation length, there is more work to do on the proper materials for Geant

## Slide 15: Sectors & Ladders as implemented

## Slide 16: Final comments
Production Sectors and ladders yet to be build. The are choices to be made for CF cloth, ladder carbon backing, so details on layers thickness and material will likely change.
What will not change is the inner surface of the sectors since the tooling equipment (mandrel) is built.
The engineering run will use a Cu-Kapton cable while the production PXL will use a Al-Kapton.

## Slide 17: Extras

## Slide 19: Radiation lengths
It is relatively easy within the Tgeo to pull out radiation lengths. The stressGeometry.C provides an example of to do such calculations using the TGeoManager. This was implemented in the assembly script to generate a first phi-distribution of radlenght at different radii.
In course of this I identified an error in the script (found by googling) The radlength in TGeo is given in cm not in g/cm**2.
The TGeoMaterial methods have the peculiar feature that if you want to set a specific length e.g. for CF with different densities you specify the Rad you want as a negative number otherwise it calculate the default from A,Z and rho (how stupid).

## Slide 20: Radiation Length at 2, 3 and 9 cm radius