## Slide 1: F.Videbaek
PXL geometry update

## Slide 2: PXL ladder
For realistic simulation it is essential to get the proper layout of ladders.
Starting point
  SW model
  Material budget from Leo

## Slide 3
Si-layer with inactive frames
Al-Kapton Cable
Carbon backing
Layers of adhesive

## Slide 4
Si 2 mil (0.0529%)
acrylic 2 mil (0.0148%)
sensor
cable
backer
support
beam
acrylic 2 mil (0.0148%)
acrylic 2 mil (0.0148%)
Al 0.7 mil (0.0124%)
kapton 1mil (0.0073%)
Al 0.7 mil (0.0124%)
Al 0.7 mil (0.0124%)
kapton 1mil (0.0073%)
Al 0.7 mil (0.0124%)
10 mil carbon composite
open weave (0.0587%)
4 mil silicon adhesive
(0.0469%)
9.6 mil carbon composite
sector beam (0.1017%)
0.0677%
0.079%
0.223 mm
0.2221%
TOTAL = 0.3688 % X0
Notes: Curtsey Leo

## Slide 5: Cable
Note that cable layout is slightly different 2 layer Al with total 0.073%.
Implemented Cable si component in my scripts using TGeo.
Materials for this have proper Radlenght, there is more work to do on the proper materials for Geant.

## Slide 6: Ladders as implemented

## Slide 8: End and top view

## Slide 9: Radiation Length at 2, 3 and 9 cm radius