## Slide 1
Spiros Margetis (Kent State Univ.)
for the STAR Collaboration
STAR Heavy Flavor Tracker
ICNFP2014, August 5, 2014, Crete, Greece

## Slide 2
2
Outline
Physics motivation
Design
  Heavy Flavor Tracker
  PiXeL detector
  Monolithic Active Pixel Sensors
Status and performance
  Status
  Efficiency
  Survey and alignment
  Hit residual and track DCA
Summary

## Slide 3
3
Physics Motivation
Heavy flavor
  mb,c >> TC, ΛQCD, mu,d,s
  Produced early in initial hard scatterings Good probe to QGP
  Total number conserved in system evolution at RHIC
However, it’s also difficult to study heavy flavor quarks in experiments
  Limited yield comparing with light flavor particles
  Short lifetimes, large combinatorial background for direct reconstruction of open heavy flavor hadrons without displaced decay vertex reconstruction
  Large kinematics smearing for studies with electrons from semi-leptonic decay
A precision vertex detector will be an important tool to assess HF physics.

## Slide 4
4
HFT can be used to study heavy flavor production by reconstruction of displaced decay vertices
  D0 → K- π+
    BR = 3.83 % cτ ~ 120 μm
  → p K- π+
    BR = 5.0 % cτ ~ 60 μm
  B mesons → J/ψ + X or e + X
    cτ ~ 500 μm
How Heavy Flavor Tracker Helps
without HFT
arXiv:1404.6185
simulation with HFT
s/(s+b) = 0.0001

## Slide 5
5
projection of D0 RCP with HFT
Total charm yield baseline for charmonium suppression & coalescence
RCP, RAA energy loss mechanism, QCD in dense medium
Charm collectivity degree of light flavor thermalization
Low radiation length enables reconstruction of D0 down to very low pT, enabling more direct and precise measurement of total charm cross section and charm flow.
Separating charm and beauty probing the medium with heavy quarks with different masses
Examples of Physics with HFT
projection of D0 v2 with HFT
simulation of separating prompt and B decayed J/ψ with HFT
HFT CDR (STAR Note SN0600)

## Slide 6
HFT in STAR
6
Tracking & dE/dx:
Time Projection Chamber
Particle ID:
Time Of Flight detector
Heavy Flavor Tracker (run 14)
Electromagnetic Calorimetry:
Barrel EMC
+Endcap EMC
Muon Telescope Detector (runs 13/14)
Full azimuthal particle identification at mid-rapidity

## Slide 7
7
Intermediate Silicon Tracker:
single-sided double-metal silicon pad
sensors with 600 μm × 6 mm pitch
σr-φ: 170 μm σz: 1800 μm
radius: 14 cm X/X0 < 1.5 %
The task of SSD and IST is to connect the tracks from the TPC to PXL in a high hit density environment.
Silicon Strip Detector:
existing detector with new faster electronics
double sided silicon strip modules with 95 μm pitch
σr-φ: 20 μm
σz: 740 μm
radius: 22 cm
X/X0: 1 %
HFT Design

## Slide 8
8
Pixel Detector Design
PIXEL detector
10 sectors * 4 ladders (1 inner + 3 outer) * 10 Monolithic Active Pixel Sensors (MAPS)
  20.7 μm pixel pitch
  thinned down to 50 μm
  used in a collider experiment for the first time
light carbon fiber support
radius:
  2.9 cm (inner)
  8.2 cm (outer)
σ:
= 7.8 μm vibration
X/X0: 0.4 % / layer
360 M pixels in total
air cooled
3 kinematic mounts locate the PXL half on the PXL supporting tube.
xyz constraint
xy constraint
x constraint
PXL insertion can be done in ~12 hours, by pushing PXL halves along rails and latching on kinematic mounts.
2 sets of PXL detectors and 40 spare ladders are made, to replace damaged detector units when needed.

## Slide 9
9
MAPS pixel cross-section (not to scale)
Monolithic Active Pixel Sensors
standard commercial CMOS technology
sensor and signal processing are integrated in the same silicon wafer
discriminator & zero suppression in sensor, readout raw hits directly
  integration time 185.6 μs
  Reticle size (~ 4 cm²)
  928 x 960 ~= 890 k pixels
  Pixel pitch 20.7 μm
signal mainly from thermal diffusion in the low-doped epitaxial layer (10~15 μm)
100 % fill-factor
MIP signal < 1000 electrons
collected in large E-field depleted region
Correlated Double Sampling
Developed by PICSEL group of IPHC-Strasbourg.
(Marc Winter et al.)

## Slide 10
10
HFT Status
Cosmic event Au+Au 200 GeV event
The full system has been installed ahead of RHIC 2014 running to take cosmic data for alignment (before Feb. 9 and whenever there is long time with no beam). We also tested 3 PXL sectors in Run-13.
Some detector performance optimization was done during the 14.5 GeV Au+Au run (Feb. 14 ~ Mar. 11)
200 GeV Au+Au data taking with PXL and IST started in March 15. Collected ~1.2 Billion events.
SSD commissioned later in the run – collected about 172 Million events.

## Slide 11
11
layer | inactive units
PXL inner | 14 %
PXL outer | 1 %
IST | 4 %
Z vs. φ of IST hits
Most PXL sensor damages appear to be radiation related damage possibly due to latch up in thinned sensors.
  Minimal or no damage for > 1 month: our operational methods were successful at stopping or greatly reducing the rate of damage.
  PXL and IST are only turned on when collision rate < 55 kHz.
  the full PXL detector resets every 15 minutes
  Latch up thresholds changed from 400 mA to 120 mA above the measured operating current for each ladder
Damage and Remediation
Z vs. φ of hits in PXL inner layer Z vs. φ of hits in PXL outer layer
100 inner sensors in total

## Slide 12
12
IST efficiency measured with cosmic ray: hits / projection
Average = 98.6 %
Tuning for including HFT in tracking is going on…
Efficiency
PXL sensor efficiency measured with cosmic ray: hits / projection
Before the detector response optimization and running with the beam
Average = 97.2 %
Low statistics of near horizontal cosmics

## Slide 13
Survey and Alignment
Coordinate Measurement Machine is used to survey HFT detector parts.
13
PXL sensor surface profile from survey
+- 30 μm > PXL hit error
Survey fixed sensor-on-ladder and ladders-on-sectors plus surface profiles (PXL)
Repeatability/time dependences were found to be ~10 microns
Similar work was done for SSD, IST
Alignment fine tuned sector-on-half and half-to-half positioning in-situ
  Self (relative) PXL alignment based on track projection and reconstructed vertex/sector analysis
SSD/IST adjusted to PXL

## Slide 14
Survey and Alignment
14
Cosmic ray and Low Luminosity data are used to align and monitor different HFT detector parts
Widths are compatible with expected extrapolation errors (hit resolution+MCS)
PXL hit residual distribution before and after alignment
IST hit residual distribution before and after alignment

## Slide 15
Track DCA
15
DCA resolution vs. momentum (averaged over phi) for pion, kaon and proton tracks with 1 IST hit + 2 PXL hits
~ 30 μm at high pT
Achieved CD4 goal: <60 μm for kaon with pT = 750 MeV/c

## Slide 16
Summary
STAR Heavy Flavor Tracker will enable or enhance many open heavy flavor measurements, by reconstructing open heavy flavor hadrons with displaced decay vertices.
State-of-art MAPS technology is used for the first time in a collider experiment in the PXL detector.
All 3 sub-detectors (PXL, IST, SSD) were assembled and inserted into STAR before RHIC year 2014 running.
With survey and preliminary alignment, we already achieved ~30 microns pointing resolution for high pT tracks reconstructed with HFT hits.
Data taking with PXL and IST reached our goal for Run-14. p+p 200 GeV and more Au+Au data will come in runs 15 & 16.
New physics results with HFT will greatly enhance our understanding of QGP created at RHIC.

## Slide 17
END

## Slide 18
Extra Slides

## Slide 19
19
IST Pedestal
RMS noise
signal to noise ratio ~ 23
Noise data for PXL and pedestal data for IST and SSD are taken at least once per day without beam, to monitor PXL noise rate, hot pixels, and calibrate IST pedestal.
IST signal with MIP
MVP ~ 440 ADCs
See details at poster M-30 by Yaping Wang
Optimize sub-array thresholds in a PXL sensor for noise rate = 2.e-6
Signal, Pedestal and Noise Scan
IST has stable pedestal and RMS level over all channels
5 2.5 0 -2.5 -5 -7.5
threshold with respect to current value (mV)
noise rate
Qiu Hao

## Slide 20
Tracking & dE/dx:
Time Projection Chamber
Particle ID:
Time Of Flight detector
Heavy Flavor Tracker (run 14)
Electromagnetic Calorimetry:
Barrel EMC
+Endcap EMC
+Forward Meson Spectrometer
(-1 ≤  ≤ 4)
Muon Telescope Detector (runs 13/14)
Forward GEM Tracker (runs 12/13)
20
STAR Detector Overview
Full azimuthal particle identification at middle rapidity

## Slide 21
21
HFT Design
SSD
IST
PXL
HFT

## Slide 22
22
HFT Status
Engineering run for PXL prototype (3 out of 10 sectors) finished
  installed on May 8, 2013
    within 12 hours
  first PXL data in daq file on May 10
  78 M events taken with PXL
full system to be installed in 2014
IST ladder
PXL prototype half
SSD part
PXL prototype insertion

## Slide 23
PXL Performance
2D correlation between measured pxl hit and TPC track projection on a sensor
Double difference of hit and track projection positions between 2 overlapping sensors
Single sensor resolution = 20 / √2 = 14 microns ~ 12 microns resolution of designed goal
23

## Slide 24
STAR Beam User Request, endorsed by RHIC PAC.
Focus on 200 GeV AA, pA, and pp collisions for heavy ion programs with new upgrades.
RHIC Run Plan

## Slide 25
25
IST Pedestal
RMS noise
signal to noise ratio ~ 23
Noise data for PXL and pedestal data for IST and SSD are taken at least once per day without beam, to monitor PXL noise rate, hot pixels, and calibrate IST pedestal.
IST signal with MIP
MVP ~ 440 ADCs
Optimize sub-array thresholds in a PXL sensor for noise rate = 2.e-6
Signal, Pedestal and Noise Scan
IST has stable pedestal and RMS level over all channels
5 2.5 0 -2.5 -5 -7.5
threshold with respect to current value (mV)
noise rate

## Slide 26
26
Charm Yield, RCP and RAA
Large combinatorial background using primary tracks to reconstruct D0
Much better S/B ratio with displaced vertex from HFT
simulation with HFT
simulation with HFT
HFT CDR (STAR Note SN0600)
arXiv:1404.6185; subm. to PRL

## Slide 27
27
Charm Yield, RCP and RAA
Total charm yield base line for charmonium suppression & coalescence
RCP, RAA energy loss mechanism, QCD in dense medium
arXiv:1404.6185; subm. to PRL

## Slide 28
28
Charm Flow
Charm collectivity light flavor thermalization?
D0 v2 is a more direct measurement of charm flow than non-photonic electron v2.
With HFT STAR is able to measure D0 v2 at low pT region, which is sensitive to charm flow.
STAR projection with HFT
Nucl.Phys.A904-905 2013 (2013) 665c-668c
HFT CDR (STAR Note SN0600)

## Slide 29
29
Charm Yield, RCP and RAA
Much better precision with HFT than current STAR measurement
Low radiation length enable reconstruction of D0 with pT starting from ~0, enabling charm total cross section measurement.
STAR projection with HFT
arXiv:1404.6185; subm. to PRL
HFT CDR (STAR Note SN0600)

## Slide 30
30
Charm Yield, RCP and RAA
JHEP09(2012)112
Probe possible different medium property with different collision energy.
STAR projection with HFT

## Slide 31
31
Charm Flow
Charm collectivity light flavor thermalization?
Measurements at both LHC and RHIC will explore the change of media properties with energy.
arXiv:1305.2707
Phys. Rev. Lett. 111 (2013) 102301
STAR projection with HFT
HFT CDR (STAR Note SN0600)

## Slide 32
32
HFT Physics Motivation
HFT can be used to study heavy flavor production by the measurement of displaced vertices
  D0 → K- π+
    BR = 3.83 % cτ ~ 120 μm
  → p K- π+
    BR = 5.0 % cτ ~ 60 μm
  B mesons → J/ψ + X or e + X
    cτ ~ 500 μm
Total charm yield base line for charmonium suppression & coalescence
RCP, RAA of charm and bottom energy loss in QGP
Charm (D0) flow thermalization?
( ) angular correlation interaction with the medium
/D0 test coalescence model

## Slide 33
33
Charm Yield, RCP and RAA
Much better precision with HFT than current STAR measurement
Low radiation length enable reconstruction of D0 with pT starting from ~0, enabling charm total cross section measurement.
STAR projection with HFT
arXiv:1404.6185; subm. to PRL
HFT CDR (STAR Note SN0600)

## Slide 34
34
Charm Yield, RCP and RAA
JHEP09(2012)112
Probe possible different medium property with different collision energy.
STAR projection with HFT

## Slide 35
35
Charm Flow
Charm collectivity light flavor thermalization?
Measurements at both LHC and RHIC will explore the change of media properties with energy.
arXiv:1305.2707
Phys. Rev. Lett. 111 (2013) 102301
STAR projection with HFT
HFT CDR (STAR Note SN0600)