## Slide 1
Spiros Margetis (Kent State Univ.)
for the STAR Collaboration
STAR Heavy Flavor Tracker
QCD@WORK, Bari, Italy 2014

## Slide 2
2
Outline
Physics motivation
Design
  Heavy Flavor Tracker
  PiXeL, IST, SSD detectors
Status and performance
  Status
  Efficiency
  Survey and alignment
  Hit residual and track DCA
Summary

## Slide 3
3
Physics Motivation
Heavy flavor
  mb,c >> TC, ΛQCD, mu,d,s
  Produced early in initial hard scatterings Good probe to QGP
  Total number conserved in system evolution at RHIC
However, it’s also difficult to study heavy flavor quarks in experiments
  Limited yield comparing with light flavor particles
  Short lifetimes, large combinatorial background for direct reconstruction of open heavy flavor hadrons without displaced decay vertex reconstruction
  Large kinematics smearing for studies with electrons from semi-leptonic decay
A precision vertex detector will be an important tool to asses HF physics.

## Slide 4
4
HFT Physics Motivation
HFT can be used to study heavy flavor production by the measurement of displaced vertices
  D0 → K- π+
    BR = 3.83 % cτ ~ 120 μm
  → p K- π+
    BR = 5.0 % cτ ~ 60 μm
  B mesons → J/ψ + X or e + X
    cτ ~ 500 μm
Total charm yield base line for charmonium suppression & coalescence
RCP, RAA of charm and bottom energy loss in QGP
Charm (D0) flow thermalization?
( ) angular correlation interaction with the medium
/D0 test coalescence model

## Slide 5
5
Charm Yield, RCP and RAA
Total charm yield base line for charmonium suppression & coalescence
RCP, RAA energy loss mechanism, QCD in dense medium
arXiv:1404.6185; subm. to PRL

## Slide 6
6
Charm Yield, RCP and RAA
Large combinatorial background using primary tracks to reconstruct D0
Much better S/B ratio with displaced vertex from HFT
simulation with HFT
simulation with HFT
HFT CDR (STAR Note SN0600)
arXiv:1404.6185; subm. to PRL

## Slide 7
7
Charm Yield, RCP and RAA
Much better precision with HFT than current STAR measurement
Low radiation length enable reconstruction of D0 with pT starting from ~0, enabling charm total cross section measurement.
STAR projection with HFT
arXiv:1404.6185; subm. to PRL
HFT CDR (STAR Note SN0600)

## Slide 8
8
Charm Yield, RCP and RAA
JHEP09(2012)112
Probe possible different medium property with different collision energy.
STAR projection with HFT

## Slide 9
9
Charm Flow
Charm collectivity light flavor thermalization?
D0 v2 is a more direct measurement of charm flow than non-photonic electron v2.
With HFT STAR is able to measure D0 v2 at low pT region, which is sensitive to charm flow.
STAR projection with HFT
Nucl.Phys.A904-905 2013 (2013) 665c-668c
HFT CDR (STAR Note SN0600)

## Slide 10
10
Charm Flow
Charm collectivity light flavor thermalization?
Measurements at both LHC and RHIC will explore the change of media properties with energy.
arXiv:1305.2707
Phys. Rev. Lett. 111 (2013) 102301
STAR projection with HFT
HFT CDR (STAR Note SN0600)

## Slide 11
11
J/ψ from B meson
simulation with HFT
Measured before through J/ψ-hadron correlation
  only in p-p collisions
  large errors
with HFT can be measured by displaced vertex
with MTD can also be measured through μ+μ- channel
Phys. Lett. B 722 (2013) 55

## Slide 12
HFT in STAR
12
Tracking & dE/dx:
Time Projection Chamber
Particle ID:
Time Of Flight detector
Heavy Flavor Tracker (run 14)
Electromagnetic Calorimetry:
Barrel EMC
+Endcap EMC
Muon Telescope Detector (runs 13/14)
Full azimuthal particle identification at mid-rapidity

## Slide 13
13
Intermediate Silicon Tracker:
single-sided double-metal silicon pad
sensors with 600 μm × 6 mm pitch
σr-φ: 170 μm σz: 1800 μm
radius: 14 cm X/X0 < 1.5 %
The task of SSD and IST is to guide the track from TPC to the innermost PXL detector with high hit density.
Silicon Strip Detector:
existing detector with new faster electronics
double sided silicon strip modules with 95 μm pitch
σr-φ: 20 μm
σz: 740 μm
radius: 22 cm
X/X0: 1 %
HFT Design

## Slide 14
14
Pixel Detector Design
PIXEL detector
10 sectors * 4 ladders (1 inner + 3 outer) * 10 Monolithic Active Pixel Sensors (MAPS)
  20.7 μm pixel pitch
  thinned down to 50 μm
  used in a collider experiment for the first time
light carbon fiber support
radius:
  2.9 cm (inner)
  8.2 cm (outer)
σ:
= 7.8 μm vibration
X/X0: 0.4 % / layer
360 M pixels in total
air cooled
3 kinematic mounts locate the PXL half on the PXL supporting tube.
xyz constraint
xy constraint
x constraint
PXL insertion can be done in ~12 hours, by pushing PXL halves along rails and latching on kinematic mounts.
2 sets of PXL detectors and 40 spare ladders are made, to replace damaged detector units when needed.

## Slide 15
15
MAPS pixel cross-section (not to scale)
Monolithic Active Pixel Sensors
standard commercial CMOS technology
sensor and signal processing are integrated in the same silicon wafer
discriminator & zero suppression in sensor, readout raw hits directly
  integration time 185.6 μs
  Reticle size (~ 4 cm²)
  928 x 960 ~= 890 k pixels
  Pixel pitch 20.7 μm
signal mainly from thermal diffusion in the low-doped epitaxial layer (10~15 μm)
100 % fill-factor
MIP signal < 1000 electrons
collected in large E-field depleted region
Correlated Double Sampling
Developed by PICSEL group of IPHC-Strasbourg.
(Marc Winter et al.) Thank you!

## Slide 16
16
HFT Status
a cosmic event a Au+Au 200 GeV event
The full system has been installed ahead of RHIC 2014 running to take cosmic data for alignment (before Feb. 9 and whenever there is long time with no beam). We also tested 3 PXL sectors in Run-13.
Some detector performance optimization was done during 14.5 GeV Au+Au run (Feb. 14 ~ Mar. 11)
200 GeV Au+Au data taking with PXL and IST since March 15. Collected ~1.2 Billion events so far.
SSD commissioned later in the run – collected about 150 Million events so far.

## Slide 17
17
layer | inactive units
PXL inner | 14 %
PXL outer | 1 %
IST | 4 %
Z vs. φ of IST hits
Most PXL sensor damages appears to be radiation related damage possibly due to latch up in thinned sensors.
  Minimal or no damage for > 1 month: our operational methods were successful at stopping or greatly reducing the rate of damage.
  PXL and IST are only turned on when collision rate < 55 kHz.
  the full PXL detector resets every 15 minutes
  Latch up thresholds changed from 400 mA to 120 mA above the measured operating current for each ladder
Damage and Remediation
Z vs. φ of hits in PXL inner layer Z vs. φ of hits in PXL outer layer
100 inner sensors in total

## Slide 18
18
IST efficiency measured with cosmic ray: hits / projection
~ 95 % at operational threshold / noise
Tuning for including HFT in tracking is going on…
Efficiency
PXL sensor efficiency measured with cosmic ray: hits / projection
Before the detector response optimization and running with the beam
Average = 97.2 %
Low statistics of near horizontal cosmic operational threshold / noise = 5

## Slide 19
Survey and Alignment
Coordinate Measurement Machine is used to survey HFT detector parts.
19
PXL sensor surface profile from survey
+- 30 μm > PXL hit error
PXL hit residual distribution before and after PXL half to half alignment
Cosmic ray is used to align different HFT detector parts.

## Slide 20
Hit Residual and Track DCA
20
IST hit residuals to cosmic track projection: σx = 200 μm, σz = 1800 μm
match IST pad size
DCA resolution for tracks with TPC + 1 IST hit + 2 PXL hits
~ 30 μm at high pT
Below project goal: 60 μm for kaon with pT = 750 MeV/c
PXL hit residual to cosmic track projection after PXL sector alignment: σ < 25 μm, match the design goal

## Slide 21
Summary
STAR Heavy Flavor Tracker will enable or enhance many open heavy flavor measurements, by reconstructing open heavy flavor hadrons with displaced decay vertices.
State-of-art MAPS technology is used for the first time in a collider experiment in the PXL detector.
All 3 sub-detectors (PXL, IST, SSD) are finished with construction and inserted into STAR before RHIC year 2014 running.
With survey and preliminary alignment, we already achieved ~30 microns pointing resolution for high pT tracks reconstructed with HFT hits.
Data taking with PXL and IST reached our goal for this year. p+p 200 GeV and more Au+Au data will come in runs 15 & 16.
New physics results with HFT will greatly enhance our understanding of QGP created at RHIC.

## Slide 22
Back Up

## Slide 23
Tracking & dE/dx:
Time Projection Chamber
Particle ID:
Time Of Flight detector
Heavy Flavor Tracker (run 14)
Electromagnetic Calorimetry:
Barrel EMC
+Endcap EMC
+Forward Meson Spectrometer
(-1 ≤  ≤ 4)
Muon Telescope Detector (runs 13/14)
Forward GEM Tracker (runs 12/13)
23
STAR Detector Overview
Full azimuthal particle identification at middle rapidity

## Slide 24
24
HFT Design
SSD
IST
PXL
HFT

## Slide 25
25
HFT Status
Engineering run for PXL prototype (3 out of 10 sectors) finished
  installed on May 8, 2013
    within 12 hours
  first PXL data in daq file on May 10
  78 M events taken with PXL
full system to be installed in 2014
IST ladder
PXL prototype half
SSD part
PXL prototype insertion

## Slide 26
PXL Performance
2D correlation between measured pxl hit and TPC track projection on a sensor
Double difference of hit and track projection positions between 2 overlapping sensors
Single sensor resolution = 20 / √2 = 14 microns ~ 12 microns resolution of designed goal
26

## Slide 27
STAR Beam User Request, endorsed by RHIC PAC.
Focus on 200 GeV AA, pA, and pp collisions for heavy ion programs with new upgrades.
RHIC Run Plan

## Slide 28
28
IST Pedestal
RMS noise
signal to noise ratio ~ 23
Noise data for PXL and pedestal data for IST and SSD are taken at least once per day without beam, to monitor PXL noise rate, hot pixels, and calibrate IST pedestal.
IST signal with MIP
MVP ~ 440 ADCs
Optimize sub-array thresholds in a PXL sensor for noise rate = 2.e-6
Signal, Pedestal and Noise Scan
IST has stable pedestal and RMS level over all channels
5 2.5 0 -2.5 -5 -7.5
threshold with respect to current value (mV)
noise rate