## Slide 1: Upgrade of the STAR silicon detectors
Institut Pluridisciplinaire Hubert Curien (IPHC-CNRS), Strasbourg, France
Michal Szelezniak for the STAR collaboration

## Slide 2: Outline
STAR HFT
  3 sub-detectors
PXL Detector
  First MAPS based vertex detector
HFT status and performance
PXL detector – Lessons Learned
Summary and Outlook
RHIC at BNL, Upton, NY
STAR experiment
STAR HFT

## Slide 3: STAR Heavy Flavor Tracker (HFT) Upgrade
Built to identify mid rapidity Charm and Beauty mesons and baryons through direct reconstruction and measurement of the displaced vertex with excellent pointing resolution.
TPC – Time Projection Chamber (main tracking detector in STAR)
HFT – Heavy Flavor Tracker
SSD – Silicon Strip Detector
IST – Intermediate Silicon Tracker
PXL – Pixel Detector
 = ~1 mm
 = ~300 m
 = ~250 m
 = <30 m
SSD r = 22
IST r = 14
PXL r2 = 8
  r1 = 2.8
Tracking inwards graded resolution:
R (cm)

## Slide 4: Silicon Strip Detector (SSD)
Double sided silicon strip modules with 95 μm pitch
Existing detector with new faster electronics
Radius: 22 cm
Radiation length 1% X0

## Slide 5: SSD refurbishment
20 ladders from the old SSD detector
Upgrade readout from 200 Hz to 1 kHz
New
  40 ladder cards on detector
  5 RDO cards
  5 Fiber-to-LVDS boards
  Upgraded cooling system (air cooled)
Ladder Cards
Fiber-to-LVDS
RDO board, adapted from PXL

## Slide 6: Intermediate Silicon Tracker (IST)
Conventional Si pad detector using CMS APV chip for ladders
Readout system copy of just completed FGT detector system
  G. Visser et al. A Readout System Utilizing the APV25 ASIC for the Forward GEM Tracker in STAR, IEEE Real Time Conference Record, Berkeley, CA, 2012
  Single sided double-metal silicon pad with 600 μm x 6 mm pitch
  Radius: 14 cm
  Radiation length <1.5% X0

## Slide 7: IST characteristics
ϕ-Coverage | 2π
¦η¦-Coverage | ≤1.2
Number of Staves | 24
Number of hybrids | 24
Number of sensors | 144
Number of readout chips | 864
Number of channels | 110592
r-ϕ resolution | 172 μm
Z resolution | 1811 μm
R-ϕ pad size | 594 μm
Z pad size | 6275 μm
~ 50 cm
300 μm Hamamatsu sensor
( 64 × 12 pads)
IST stave = Carbon fiber ladder
+ Kapton flex hybrid
+ Passive components
+ 6 silicon pad sensors
+ 3 x 12 APV25-S1 readout chips
+ Aluminum cooling tube
+ Liquid coolant (3M Novec 7200)
IST staves were assembled/tested/surveyed at UIC/FNAL and MIT/BNL sites (18 staves produced at each site).

## Slide 8: PXL detector
  MAPS sensors with 20.7 μm pitch
  Radius: 2.8 and 8 cm
  Radiation length <0.4% X0 in inner layer
first MAPS based vertex detector at a collider experiment

## Slide 9: PXL characteristics
DCA Pointing resolution * | (12  24 GeV/pc) m
Layers | Layer 1 at 2.8 cm radius Layer 2 at 8 cm radius
Pixel size | 20.7 m X 20.7 m
Hit resolution | 3.7 m (6 m geometric)
Position stability | 6 m rms (20 m envelope)
Radiation length first layer | X/X0 = 0.39% (Al conductor cable)
Number of pixels | 356 M
Integration time (affects pileup) | 185.6 s
Radiation environment | 20 to 90 kRad / year 2*1011 to 1012 1MeV n eq/cm2
Rapid detector replacement (hot spare copy of the detector) | ~ 1 day
356 M pixels on ~0.16 m2 of Silicon
* Pointing resolution is limited by MCS and mechanical stability

## Slide 10: PXL architecture
  Insertion from one side
  10 sectors total
  5 sectors / half
  4 ladders / sector
Mechanical support with kinematic mounts (insertion side)
Cantilevered support
Ladder with 10 MAPS sensors (~ 2×2 cm each)
carbon fiber sector tubes (~ 200 µm thick)

## Slide 11: PXL detector Ultimate-2 sensor
  Reticle size (~ 4 cm²)
    Pixel pitch 20.7 μm
    928 x 960 array
  Power dissipation ~170 mW/cm² @ 3.3V (air cooling)
  Short integration time 185.6 μs
  Sensors thinned to 50 µm
3rd generation sensor developed for the PXL detector
by the PICSEL group of IPHC, Strasbourg
  In pixel CDS
  Discriminators at the end of each column
  Column-parallel readout
  2 LVDS data outputs @ 160 MHz
  Integrated zero suppression (up to 9 hits/row)
  Ping-pong memory for frame readout (~1500 words)
  4 sub-arrays to help with process variation
  JTAG configuration of many internal parameters

## Slide 12: PXL detector readout chain
2 m
(42 AWG TP)
11 m (VHDCI)
100 m (fiber optic)
Highly parallel system
  4 ladders per sector
  1 Mass Termination Board (MTB) per sector
  1 RDO board per sector
  10 RDO boards in the PXL system
RDO board w/ Xilinx Virtex-6 FPGA
- event building
DAQ PC with RORC
Mass Termination Board
signal buffering
latch-up protected power
Clk, config, data, power
Clk, config, data
PXL built events
PXL Sector
- Continuous readout
Trigger,
Slow control,
Configuration,
etc.
Notes: 12

## Slide 13: PXL insertion
Unique mechanical design:
detector is inserted along rails and locks into a kinematic mount on the insertion end of the detector
Allows for rapid (1 day) replacement with a characterized spare detector
Yes – we push it in by hand
Kinematic mounts
Insertion of PXL detector

## Slide 14: HFT Status and Performance

## Slide 15: HFT Status
IST, SSD installed into STAR in the fall 2013
PXL inserted into STAR at the end of January 2014
Commissioning of HFT detectors in February and March including Cosmic Ray data taking (extended SSD commissioning)
Physics data taking March - July
Collected >1.2 Billion events
Cosmic ray
tests
PXL+IST
intermittently
PXL+IST
+ (SSD commissioning)
14.5 GeV
start
Jan
25
PXL
install
Feb
14
200 GeV
start
Mar
14
He+Au
start
Jun
19
Jul
7
End of run
IST+SSD

## Slide 16: HFT Status
SSD
  The RDO runs at <20% dead-time at 1 kHz
    The ultimate limit is due to old Si modules (circa 2000)
  6% dead wafers
  90 % of the strips are active in the remaining wafers
  Collected 172 M Au+Au events and 57 M He3+Au events
IST
  864 readout chips and 110592 channels total
  More than 95% fully functional channels
  Hit efficiency ~99%
  S/N 15:1-30:1
  Coolant leak rate 0.5-1.0% per day (to be fixed)
  Participated in data taking for He3+Au collisions

## Slide 17
Pxl installation pics
Clean room
Installed and cabled
PXL assembled in the STAR clean room @BNL
PXL inserted and cabled into the STAR TPC inner field cage
PXL installation
At installation:
PXL installed with all 400 sensors working, <2k bad pixels
38 ladders with Cu flex + 2 inner ladders with Al flex
Noise rates were tuned for ~1.5 x 10-6 per sensor for most sensors
Total installation time = 2 days

## Slide 18: PXL preliminary half-to-half pointing residuals
Consistent with expectations for alignment and momentum of muons
σ ~ 25µm for inner layer and 50µm for outer layer
Cosmic ray event
(PXL + IST)
Preliminary Preliminary Preliminary
PXL hit residual distributions before and after PXL half-to-half alignment
(analysis by A. Schmah, LBL)
Preliminary Preliminary Preliminary
Preliminary Preliminary Preliminary

## Slide 19: Preliminary DCA Pointing resolution
result from the STAR HFT software group
200 GeV Au+Au event
Preliminary
PXL preliminary half-to-half pointing residuals after sector alignment
σ < 25 µm for inner layer.
DCA resolution (TPC + IST + PXL) ~ 30 m at high pT (better alignment in progress)
CD-4 requirement for DCA resolution: 60  m for kaons with pT = 750 MeV/c

## Slide 20: PXL Detector Lessons Learned

## Slide 21: Probe testing
Thinned and diced 50 µm thick sensors
Custom made vacuum chuck
Full sensor characterization (~15 min):
  Parameter characterization at different bias V (@ 2.9V, 3V, 3.3 V)
  I/V measurements
  Bias optimization
  Temporal noise and FPN measurements
  Accidental hit rate scan
  Response to LED pulse (@ 3.3V)
Full speed readout @ 160 MHz
Automated interface to a database
Sensors built-in testing functionality
Proper probe pin design for curved thinned sensors
Yield varied 46% - 60%
Administrative control of sensor ID

## Slide 22: PXL ladder
Flex cable
(Copper version)
Classic wire bonding
Difficulties and delays with Al cable production
Backup solution with Cu cables
Cu conductor:
X/X0  to 0.129%
(corrected for the thinner copper layer)
 Cu based ladders X/X0 = 0.492%

## Slide 23: PXL ladder assembly
  Cable reference holes for assembly
Hybrid cable with carbon fiber stiffener plate on back in position to glue on sensors
  Sensor positioning
  FR-4 Handler
Precision vacuum chuck fixtures to position sensors
  by hand
  with butted edges
Acrylic adhesive prevents CTE difference based damage
DRIE dicing improves alignment
  Proposed by IPHC in order to improve sensor abuttal
DRIE trenches
Saw cut
  Assembled ladder
  30.5 cm

## Slide 24: Sector and detector half assembly
Metrology picture
Sectors
Ladders are glued on carbon fiber sector tubes in 4 steps
Pixel positions on sector are measured and related to tooling balls
Detector half
Sector assembly fixture
Sector in the metrology setup
 | ladder yield |  |  | 
 | after assembly + bonding | after encapsulation | after sector mounting | after metrology
Tested | 92 | 59 | 53 | 48
yield | 0.91 | 0.92 | 0.91 | 1.00
Initially lower yield (debugging)
Detector half
Sectors mounted in dovetail slots on detector half
Metrology to relate sector tooling balls to each other and to kinematic mounts

## Slide 25: Engineering run 2013
Sensor IR picture
Flawed ladder dissection: searching for shorts
Inner layer design
PXL Engineering Run assembly crucial to deal with a number of unexpected issues
After the engineering run added functionality to the MTB:
  remote setting of LU threshold and ladder power supply voltage + current and voltage monitoring
Shorts between power and gnd, or LVDS outputs
Adhesive layer extended in both dimensions to increase the portion coming out from underneath the sensors
Insulating solder mask added to low mass cables
Mechanical interference in the driver boards on the existing design.
The sector tube and inner ladder driver board have been redesigned to give a reasonable clearance fit
Inner layer design modification: ~ 2.8 cm inner radius
Engineering run geometry

## Slide 26
PXL radiation damage in run 2014
SEE tests were performed with earlier prototypes, not the production ones
Operational methods seem to halt radiation induced damage
Second detector will be protected from day one
24-03-2014
24-05-2014
First damage observed in the 14.5 GeV running after several beam loss events
continued into 200 GeV run
Appears to be radiation related (possibly latch-up events):
  increased digital current, damaged JTAG registers, loss of sub-arrays, etc.
  mostly in inner ladders
  (14% of inner layer, 1% of outer layer)
Remediation:
Latchup thresholds lowered to 120 mA (initially 400 mA) above measured operational current for each ladder
Cycle digital power and reload configuration automatically every 15 minutes
HFT is only turned on when collision rate < 55 kHz
Amps
“Bad” inner sensors vs time
Digital current on the inner ladders during the run 2014

## Slide 27
Summary and Outlook
STAR Heavy Flavor Tracker was installed and commissioned for the 2014 Au+Au RHIC run
The (preliminary) DCA pointing resolution performance of the installed HFT detectors appears to be as expected and meets the design goals
Observed radiation related damage in the PXL detector appears to be halted by using operational methods
The spare detector (with Al conductor cable on the inner ladders) is complete and will be deployed in the next run. We are repairing the damage to the existing detector with the spare ladders.
DOE CD-4 review is complete and the HFT upgrade meets all of the construction project performance parameters.
MAPS appear to be working well as a technology for vertex detectors
The PXL detector is the first MAPS based vertex detector and as such leads the way for future vertex detectors based on MAPS technology (such as the ALICE ITS, etc.)

## Slide 28
Thank you for you attention

## Slide 29: SSD sensors
The sensors are double sided strip detectors

## Slide 30: Silicon Strip Detector (SSD)
~ 1 Meter
44 cm
20 Ladders
Ladder Cards

## Slide 31: IST Stave

## Slide 32: PXL electronics and operator’s GUI
4V South
6V MTBs
4V North
10 RDO boards
1 Trigger distribution board
USB hub
USB<->fiber
interlocks
two-panel control interface

## Slide 33: PXL sensor development at IPHC
2011-2012
Final sensor for the PXL detector
2008
Full size sensor with digital readout
Pixel
Sensors
ADC
Data
sparsification
readout
to DAQ
analog
signals
Complementary detector readout
4 ms integration time
< 200 μs integration time
analog
digital
digital signals
640 μs integration time
CDS – Correlated Double Sampling
Three generations of sensors designed specifically for the PXL detector
PXL sensors benefited from parallel development of multiple other sensor prototypes designed and tested at IPHC
2004-2008
First MAPS prototypes for the STAR PXL detector
Finding suitable CMOS technology (AMS0.35)
Unexpected issues scaling small prototypes to half-reticule size solved by adjustments in the fabrication process
Incomplete via contacts in the middle of the chip
CDS
CDS
Disc.
sensor
generations
1st
2nd
3rd

## Slide 34: PXL sensor threshold operation point
The noise level was set at ~2 x 10-6 for the cosmic ray run. At this noise rate, the measured operating point (taken from beam tests) is shown above.

## Slide 35: PXL hit efficiency
preliminary results based on the cosmic ray data
Note: this data was taken before the final detector optimizations
Preliminary