## Slide 1: Performance and Plans for the Silicon Tracker Upgrade of the STAR Experiment at RHIC
Spiros Margetis1
for the STAR Collaboration
1Kent State University, USA

## Slide 2: Outline
STAR Heavy Flavor Tracker (HFT)
  3 sub-detectors
PXL Detector
  First MAPS1 - based vertex detector
HFT status and performance
Summary and Outlook
RHIC at BNL, Upton, NY
STAR experiment
STAR HFT
1Monolithic Active Pixel Sensor

## Slide 3: STAR Heavy Flavor Tracker (HFT) Upgrade
Built to identify mid rapidity Charm and Beauty mesons and baryons through direct reconstruction and measurement of the displaced vertex with excellent pointing resolution.
TPC – Time Projection Chamber (main tracking detector in STAR)
HFT – Heavy Flavor Tracker
SSD – Silicon Strip Detector
IST – Intermediate Silicon Tracker
PXL – Pixel Detector
 = ~1 mm
 = ~300 m
 = ~250 m
 = ~30 m
SSD r = 22
IST r = 14
PXL r2 = 8
  r1 = 2.8
Tracking inwards graded resolution:
R (cm)

## Slide 4: Silicon Strip Detector (SSD)
Double sided silicon strip modules with 95 μm pitch
Existing detector with new faster electronics
Radius: 22 cm
Radiation length 1% X0
20 ladders from the old SSD detector
Upgrade readout from 200 Hz to 1 kHz
New:
  40 ladder cards on detector
  5 New RDO cards
  Upgraded cooling system (air cooled)

## Slide 5: Intermediate Silicon Tracker (IST)
Conventional Si pad detector using CMS APV chip for ladders
Readout system copy of STAR FGT detector system
  G. Visser et al. A Readout System Utilizing the APV25 ASIC for the Forward GEM Tracker in STAR, IEEE Real Time Conference Record, Berkeley, CA, 2012
  Single sided double-metal silicon pad with 600 μm x 6 mm pitch
  Radius: 14 cm
  Liquid cooling
  Radiation length <1.5% X0

## Slide 6: PXL detector
  MAPS sensors with 20.7 μm pitch
  Radius: ~2.8 and ~8 cm
  Radiation length <0.4% X0 in inner layer
first MAPS based vertex detector at a collider experiment

## Slide 7: PXL characteristics
DCA Pointing resolution * | (12  24 GeV/pc) m
Layers | Layer 1 at 2.8 cm radius Layer 2 at 8 cm radius
Pixel size | 20.7 m X 20.7 m
Hit resolution | 3.7 m (6 m geometric)
Position stability | 6 m rms (20 m envelope)
Radiation length first layer | X/X0 = 0.39% (Al conductor cable)
Number of pixels | 356 M
Integration time (affects pileup) | 185.6 s
Radiation environment | 20 to 90 kRad / year 2*1011 to 1012 1MeV n eq/cm2
Rapid detector replacement (hot spare copy of the detector) | ~ 1 day
356 M pixels on ~0.16 m2 of Silicon
* Pointing resolution is limited by MCS and mechanical stability

## Slide 8: PXL architecture
  Insertion from one side
  10 sectors total
  5 sectors / half
  4 ladders / sector
Mechanical support with kinematic mounts (insertion side)
Cantilevered support
Ladder with 10 MAPS sensors (~ 2×2 cm each)
carbon fiber sector tubes (~ 200 µm thick)

## Slide 9: HFT Status and Performance

## Slide 10: HFT in Run-14
IST, SSD installed into STAR in the fall 2013
PXL inserted into STAR at the end of January 2014
Commissioning of HFT detectors in February and March including Cosmic Ray data taking (extended SSD commissioning)
Physics data taking March - July
Collected >1.2 Billion Au+Au @ 200 GeV events
Cosmic ray
tests
PXL+IST
intermittently
PXL+IST
+ (SSD commissioning)
14.5 GeV
start
Jan
25
PXL
install
Feb
14
200 GeV
start
Mar
14
He+Au
start
Jun
19
Jul
7
End of run
IST+SSD

## Slide 11: HFT Status – Run14
SSD
  The RDO runs at <20% dead-time at 1 kHz
    The ultimate limit is due to old Si modules (circa 2000)
  6% dead wafers
  90 % of the strips are active in the remaining wafers
  Collected 172 M Au+Au events and 57 M He3+Au events
IST
  864 readout chips and 110592 channels total
  More than 95% fully functional channels
  Hit efficiency ~99%
  S/N 15:1-30:1
  Participated in data taking for Au+Au and He3+Au collisions

## Slide 12: PXL damage in Run 2014
Inner Layer: 14% damage
(Outer layer: 1% damage)
Damage on multiple ladders in the first 2 weeks
  Increased current in the digital power circuit
  Sensor data corruptions
Loss of detector efficiency
Instability of the affected ladders
Further damage stopped by tight over-current thresholds
   latch-up as possible damage cause
Post-run investigation: latch-up tests at the 88” Cyclotron @LBL
  Measure latch-up cross-sections Vs over-current protection threshold
  Reproduce damage seen during the run
  Define a safe operation envelope for Runs 2015/2016:
    over-current threshold ≤ 120mA above operating current
Examples of sensor data corruptions

## Slide 13: PXL Alignment
Consistent with expectations for alignment and momentum of muons
σ ~ 25µm for inner layer and 50µm for outer layer
Cosmic ray event
(PXL + IST), Magnet-OFF
PXL hit residual distributions before and after PXL alignment
(analysis by A. Schmah, LBL)

## Slide 14: HFT Pointing Resolution Performance- Run 14
47mm
46mm
DCA_XY
DCA_Z
D0 analysis in Run 14 data (ongoing)
DCA pointing resolution
  Design requirement: 60mm for 750 MeV/c Kaons
  2 Al cables on inner layer
  From 2015: all Al cables
200 GeV Au+Au event

## Slide 15: HFT in Run-15
RHIC run15: Current plan
Now
Main goal is to collect p-p and p-A (reference) data
Used the refurbished PXL Run14 detector
  All aluminum cable ladders on Inner layer
  Improved protection against latch-up damage
  Only ~5% damage per layer in Run15
All HFT detectors operated well in Run15

## Slide 16: HFT dataset goals for run15
p+p
p+Au
HFT minimum bias

## Slide 17: HFT goals for Run 16
STAR/RHIC improvements vs. Run 14
  PXL equipped with the Aluminum (Al) cable for inner ladders 0.52%0.38% X0
  SSD at full speed  better track matching
  Increased luminosity fraction within |Vz|<5cm
Beam request for Run 16:
  13 weeks Au+Au 200 GeV run
  2 B minimum bias events
Physics goals:
  More differential studies on charmed hadron production
  c measurement
  Open bottom measurements through B->e and B->J/psi

## Slide 18
Summary and Outlook
STAR Heavy Flavor Tracker was first fully installed and commissioned for the 2014 Au+Au RHIC run. This data set is now in production for physics analysis.
The (preliminary) DCA pointing resolution performance of the installed HFT detectors appears to be as expected and meets the design goals
Observed radiation related damage in the PXL detector appears to be halted by using operational methods
A spare detector (with Al conductor cable on the inner ladders) is complete and ready to be deployed as needed.
MAPS is working well as a technology for vertex detectors
The PXL detector is the first MAPS based vertex detector and as such leads the way for future vertex detectors based on MAPS technology (such as the ALICE ITS, etc.)

## Slide 19
Thank you!

## Slide 20
Backup Slides

## Slide 21: IST characteristics
ϕ-Coverage | 2π
¦η¦-Coverage | ≤1.2
Number of Staves | 24
Number of hybrids | 24
Number of sensors | 144
Number of readout chips | 864
Number of channels | 110592
r-ϕ resolution | 172 μm
Z resolution | 1811 μm
R-ϕ pad size | 594 μm
Z pad size | 6275 μm
~ 50 cm
300 μm Hamamatsu sensor
( 64 × 12 pads)
IST stave = Carbon fiber ladder
+ Kapton flex hybrid
+ Passive components
+ 6 silicon pad sensors
+ 3 x 12 APV25-S1 readout chips
+ Aluminum cooling tube
+ Liquid coolant (3M Novec 7200)
IST staves were assembled/tested/surveyed at UIC/FNAL and MIT/BNL sites (18 staves produced at each site).

## Slide 22: PXL sensor threshold operation point
The noise level was set at ~2 x 10-6 for the cosmic ray run. At this noise rate, the measured operating point (taken from beam tests) is shown above.

## Slide 23: Engineering run 2013
Sensor IR picture
Flawed ladder dissection: searching for shorts
Inner layer design
PXL Engineering Run assembly crucial to deal with a number of unexpected issues
After the engineering run added functionality to the MTB:
  remote setting of LU threshold and ladder power supply voltage + current and voltage monitoring
Shorts between power and gnd, or LVDS outputs
Adhesive layer extended in both dimensions to increase the portion coming out from underneath the sensors
Insulating solder mask added to low mass cables
Mechanical interference in the driver boards on the existing design.
The sector tube and inner ladder driver board have been redesigned to give a reasonable clearance fit
Inner layer design modification: ~ 2.8 cm inner radius
Engineering run geometry

## Slide 24: PXL hit efficiency
preliminary results based on the cosmic ray data
Note: this data was taken before the final detector optimizations
Preliminary

## Slide 25: PXL insertion
Unique mechanical design:
detector is inserted along rails and locks into a kinematic mount on the insertion end of the detector
Allows for rapid (1 day) replacement with a characterized spare detector
Yes – we push it in by hand
Kinematic mounts
Insertion of PXL detector

## Slide 26: PXL ladder
Flex cable
(Copper version)
Classic wire bonding
Difficulties and delays with Al cable production
Backup solution with Cu cables
Cu conductor:
X/X0  to 0.129%
(corrected for the thinner copper layer)
 Cu based ladders X/X0 = 0.492%