## Slide 1
HFT Update
S. Margetis, Kent State University STAR Regional Meeting, February 11, 2015, Prague
Notes: MAPS=Monolithic Active Pixel Sensor

## Slide 2: Talk Outline
Project news
Run-15 calibrations work
Run-14 work
  Goals/Datasets/Timeline
  Calibrations update
  Embedding
STI [tracker] work
  Geometry
  Tracking
Summary

## Slide 3: Heavy Flavor Tracker (HFT) [for the students]
SSD
IST
PXL
HFT
Detector | Radius (cm) | Hit Resolution R/ - Z (m - m) | Radiation length
SSD | 22 | 20 / 740 | 1% X0
IST | 14 | 170 / 1800 | <1.5 %X0
PIXEL | 8 | 12/ 12 | ~0.5 %X0
 | 2.8 | 12 / 12 | ~0.4% X0
SSD
existing single layer detector, double side strips (electronic upgrade)
IST
one layer of silicon strips along beam direction, guiding tracks from the SSD through PIXEL detector. - proven strip technology
PIXEL
two layers
20.7x20.7 m pixel pitch
10 sector, delivering ultimate pointing resolution that allows for direct topological identification of charm.
new monolithic active pixel sensors (MAPS) technology

## Slide 4: Heavy Flavor Tracker (HFT) [for the students]
Direct topological reconstruction of Charm
  Detect charm decays with small c, including D0  K 
Method: Resolve displaced vertices (50-100 microns)
We track inward from the TPC with graded resolution:
TPC
SSD
IST
PXL
~1mm
~300µm
~250µm
vertex
~30µm
Notes: Highlight detecting short lived particles –
you have heard about the physics in previous talks

## Slide 5: Project News
Project is completed but DOE reporting is not
Still have quarterly meetings [last was in January] to report on:
  Performance Parameter Status (UPP)
  Run preparation status [hardware/software]
  Operations during each run [data sets, problems]
  Post-run Calibrations and Analysis activities

## Slide 6: Performance parameters

## Slide 7
40um
40um
Low Luminosity Sector 6-7 (Aluminum only) -90<phi<-20

## Slide 8
Efficiency [CD4 Simulation]
UPP might be reachable
Emphasizes the role of SSD
Limiting efficiency [keep for later]

## Slide 9: Run-15
Goals/Datasets/Timelines
Calibrations
  Db Init for Geometry etc.
  Alignment of HFT elements
  Masking/noise/book-keeping
  Recent work [SSD CommonModeNoise[CMN], masking]

## Slide 10: Goals/Datasets/Timeline
Initial cosmic runs for Alignment/Masking etc are done
  Codes are being put together for production
  SSD is included in the chain
  It will take a couple of weeks to finish production and a few more to do alignment for all subsystems [SSD too for first time]
p-p 200GeV beams just started
  detectors are setup/checked
Goal is to get a good sample of p-A and p-p 200GeV [reference] data

## Slide 11: Cosmics Run-15
All 4 layers of HFT show hits correlated with TPC tracks
Self-Alignment etc can be done for all detectors
https://drupal.star.bnl.gov/STAR/blog/dongx/run15-cosmic-run-test

## Slide 12: Cosmics Run-15
TPC t0 and drift velocity need fine tuning
Stay tuned for Alignment results soon
https://drupal.star.bnl.gov/STAR/blog/dongx/run15-cosmic-run-test

## Slide 13: Run-14
Goals/Datasets/Timelines
Calibrations
  Alignment of HFT elements
  Masking/noise/book-keeping
  Recent work [SSD CMN]
STI [tracking]
  Geometry work
  Tracking efficiency optimization
  Timing issues

## Slide 14: Goals/Datasets/Timeline
We have 1.2 Billion Au+Au @ 200 GeV/c events on tape with PXL+IST
  170 M with the SSD
We have QM15 in September
Most subsystem calibrations were done back in November
But…Sti tracking with HFT not trivial. We encountered several problems:
  DCA charge asymmetries
  Speed issues
  Low tracking efficiency
Most are resolved now [next slides]
  We can live with some remaining issues
  preproduction test begun to verify masking
  production will begin very soon
  goal is to have 500Mevents ready for analysis of D0s
  Flow/RCP [~efficiency correction independent] the obvious physics goals

## Slide 15: Recent SSD work
https://drupal.star.bnl.gov/STAR/blog/bouchet/ssd-residual

## Slide 16: Recent SSD work
[left] AFTER pedestal subtraction
[right] AFTER CMN correction. CMN has external origin and affects chip level
Other work includes:
Masking tables/Gain/Algorithms/Fixes
More details here:
https://drupal.star.bnl.gov/STAR/system/files/ssdsoft_20150209_LongZhou_0.pdf
https://drupal.star.bnl.gov/STAR/event/2015/02/09/ssd-meeting

## Slide 17: Embedding

## Slide 18: Embedding
I. The edge effect:
Problem: due to differences in alignment of real geometry with respect to ideal geometry, tracks passing through inactive sensor
areas in ideal geometry do not necessarily pass through inactive sensor areas in real geometry.
Solution: I agree with your proposal to ignore all the mcHits generated by GEANT and to re-project all mcTracks on real geometry.
Check:
1. Run simulation with ideal geometry.
2. Before the HFT simulators, read all StMc*HitCollection and save their information elsewhere.
3. Clear the StMc*HitCollection.
4. Project all mcTracks on the different layers of HFT real geometry and refill the StMc*HitCollction.
5. Compare the counts from (4) to those from (2). These counts should match if the description of active/inactive sensor areas in ideal and real geometry are the same.
II. TPC simulators possible bias:
Problem: to use the mcTracks projection on HFT layers we need to understand any possible biases to the mcTracks
due to whatever happens in the TpcRS (ideal->real, calibrations, alignment, etc...). Now I could be pedantic here but I think it is worth to study.
Check: we need to see that the residuals of mcTracks projections to rcTracks projections on HFT real geometry has the expected width from finite
pointing resolution + calibrations + alignment + etc... and no systematical shifts or smearing is introduced.
1. Run embedding with TpcRS just as we would for real data but without including HFT in the tracking.
2. For every pair of mcTrack,rcTrack, project the mcTrack to the different HFT layers, call the projection mcProj. Do the same thing with the rcTrack to get rcProj.
3. Study mcProj-rcProj. These distributions should be centered around 0 and should have a width that we could understand.
We have developed a plan and we have started initial tests [simulations]

## Slide 19: STI Tracking
First let me list the people behind this effort
(Xin, Gene, Dmitri, Jason, Flemming, Hao + helpers)
Lacking a deployed version of STV we needed to use STI for Run14 production
  Needs its own, by-hand, geometry
  Needed QA/debugging/optimization for HFT environment
  It turned out to be a non-trivial task
After production starts we hope to re-assume work on STV-like tracker for several reasons [needs beyond HFT]

## Slide 20: DCA
PXL alone sort of o.k.
Mostly apparent when SSD/IST are included
Due to STI interacting with complex geometry

## Slide 21: Timing
Inclusion of HFT more than doubled time/event
Mostly when SSD/IST were included
Due to complexity/overlapping volumes in modeling
Timing issue was for both STI [shown] and Geant simulations
STI: https://drupal.star.bnl.gov/STAR/blog/jwebb/sti-timing
GEANT: https://drupal.star.bnl.gov/STAR/blog/videbaks/2014/feb/15/some-y2014-geant-timing-issues

## Slide 22
Simplification [abstraction] of geometry in non-overlapping volumes helped resolve most issues
SSD

## Slide 23
DCA problem mostly resolved
Some residual problems remain at z>30cm due to poor geometry modeling and in q/pT [charge bias]

## Slide 24
https://drupal.star.bnl.gov/STAR/blog/smirnovd/changes-increase-hft-hit-efficiency-hao
(January2015)

## Slide 25: Tracking Efficiency
Currently working with S&C to implement and test all the changes in production library
Efficiencies are high enough to start production [close to expectations]
  Work is on-going
  Some ghosting at low pt is under investigation
Longer term ideas to maximize tracking efficiency, eg CA seeding will be investigated soon
  Ivan will touch on this

## Slide 26: Summary
Physics production for part of Run-14 is about to begin
Run-15
  Calibration work underway
  Data-taking underway
  SSD is fully integrated
Get ready for Physics

## Slide 27
BACKUP SLIDES

## Slide 28: Timing
GEANT: https://drupal.star.bnl.gov/STAR/blog/videbaks/2014/feb/15/some-y2014-geant-timing-issues

## Slide 29: State of the Prototype - Example of QA plots
Several sensors were damaged during construction (red squares) and several were having hot pixels/column/rows (red dots and line)
A method to catalog and remove these noisy parts during production is being developed
Data will be used to address/correct issues in full system

## Slide 30: Detector Characteristics
Pointing resolution | (12  19 GeV/pc) m
Layers | Layer 1 at 2.5 cm radius Layer 2 at 8 cm radius
Pixel size | 20.7 m X 20.7 m
Hit resolution | 6 m
Position stability | 6 m rms (20 m envelope)
Radiation length per layer | X/X0 = 0.37%
Number of pixels | 356 M
Integration time (affects pileup) | 185.6 s
Radiation environment | 20 to 90 kRad 2*1011 to 1012 1MeV n eq/cm2
Rapid detector replacement | ~ 1 day
356 M pixels on ~0.16 m2 of Silicon

## Slide 31: CD-4 performance parameters
1 | Thickness of first PXL layer | < 0.6% X0 (0.37% in the baseline design) | Measured during construction
2 | Internal alignment and stability PXL | < 30 m (This requirement is met in the baseline mechanical design, verified by simulation and prototype testing) | Measure during prototype testing and with test beam or cosmic rays after construction.
4 | PXL integration time | < 200 s (Current generation sensors have an integration time of 185.6 s) | This is a design parameter of the sensor. This can be demonstrated with oscilloscope measurements.
5 | Detector hit efficiency PXL | 95% sensor efficiency and noise from all sources < 10-4 (Prototype sensors measured in beam tests to be > 99% with noise < 10-4) | The sensor efficiency will be measured in beam tests as a function of bias settings and threshold. This will be established prior to construction.
7 | Live channels for PXL and IST | 95% (The measured good sensor live channel yield fraction is > 99% for over 90% of sensors on a wafer. We will select good sensors for production ladders) | The number of bad pixels will be measured on each mounted sensor during probe testing and verified after ladder and sector construction. The numbers will be saved to a database.
8 | PXL and IST Readout speed and dead time | <5% additional dead time @ 500 Hz average trigger rate and simulated occupancy | This can be measured in real time with simulated data for verification.
Low-level CD-4 key performance parameters: experimentally demonstrated at Project Completion
Our current design meets (and exceeds) these requirements.