## Slide 1: Overview
S. Margetis, KSU
Survey Review, BNL, May 17, 2012

## Slide 2: Outline
Task(s) overview
Hierarchy of Coordinate systems
  Required precisions in Survey
Survey structures needs/usage
  see also other talks
Alignment methods and needs
Schedule, Manpower
Open issues

## Slide 3
General Flowchart of Survey/Alignment Tasks
Sensor/Ladder Survey
Save – CVS?
Fit, get structures
Save – Db
GEANT geometry
Apply*
RawData
Apply
Alignment
Correct
Done
N
Y
Update – Db
HITS
Final Reco Pass
ForEachRun
ForEachNewSector/Ladder
Mis-align/Check Alignment software
* VMC, STV ready

## Slide 4: Task features
Anything we build or touch needs Survey
  e.g. versioning of same physical PXL sector after repairs
Survey will freeze position of sensors on ladders and ladders on sector (PXL). Help also with sector on hemisphere (PXL). For SSD/IST will freeze position of sensors on ladder
  Alignment can check for gross mistakes but never move sensors on ladder or PXL ladder on sector. Note: this has been our way, not a universal truth
Survey raw measurements can be saved externally (CVS). Geometry and fitted parameters reside in the Db with a timestamp
For each yearly Run the in-situ position of major detector elements needs to be rechecked

## Slide 5: Reference system hierarchy
STAR Magnet=STAR system
TPC system
Fixed x,y,z
Fixed-1D-rot
Float
Star Magnet defines overall system (Field map)
TPC is the first important system for HFT (relative positioning), attached to Magnet
ESC/WSC attached to TPC wheel. It defines the HFT system’s relation (as a whole) to TPC system
See next slides for systems inside the HFT complex
Beam line constraint (new) is not a factor (?)
Experts please watch following slides – I need your input/comments

## Slide 7: General Layout
IST
SSD

## Slide 8
IST
The IST and PXL is a common/co-moving system
The SSD is independent

## Slide 9: But…OSC and PST are connected(?)
PST (IST)
OSC (SSD)

## Slide 10: Eric’s system definitions
Three targets define the basic plane A
The other two B,C are defined as:
  B is normal to A
  C is normal to A.and.B
Targets are surveyed with hundreds of microns accuracy
General rule: Definition of reference center (0,0,0) should be at the center of gravity of active elements

## Slide 11: Reference system(s) issues
In general (see next talks) survey accuracy of critical components (relative pixel and sensor positions) expected to be better than minimum acceptable values
Need expected/surveyed positions of targets
  to build ‘ideal’ position Db
  Sub-millimeter accuracies acceptable -> Tracks will fix them
  Need input on anticipated (design) in-situ position errors and estimated repeatability margins. Example:
Precision requirement:
- Pixel relative to Pixel location: 20μm (RMS over entire PXL?)
- PXL detector relative to STAR coordinate system: within 200 μm (?) H.Wieman:14 Nov 2011
GEANT geometry can/should be also synchronized with Reality instead of the current ‘patch-the-hit’ scheme
  STV, VMC environment different from current Geant3

## Slide 12: Offline use of Survey Info
y (up)
z (East)
x (South)
n,b
t,g
d,a
Definitions
Survey info is used in initial Local-to-Global transforms and inverse
Done in terms of TGeoHMatrix
General form is:
This can be e.g. the center of a sensor or a hit. For PXL sensors a distortion function (TPS output) will take care of individual pixels in a wafer.
n,d,t are unit vectors and b,a,g the corresponding rotation angles, RHS
TGeoHMatrix definition
Transform example

## Slide 13
Example: $STAR/StarDb/Geometry/ssd/SsdOnGlobal.upgr01.C
WG = Tpc2Global * GL * SG * LS * WLL;
WaferInGlobal= Tpc2Global *SsdinTpc*SectorInSSD*LadderInSector*WaferInLadder
// SSD and SVT as whole
St_Survey *SsdOnGlobal = (St_Survey *) GetDataBase("Geometry/ssd/SsdOnGlobal");
Survey_st *OnGlobal = SsdOnGlobal->GetTable();
GL.SetRotation(&OnGlobal->r00);
GL.SetTranslation(&OnGlobal->t0);
// SSD sectors in SSD/SVT system
St_Survey *SsdSectorsOnGlobal = (St_Survey *) GetDataBase("Geometry/ssd/SsdSectorsOnGlobal");
// ladders in the SSD sector coordinate systems
St_Survey *SsdLaddersOnSectors = (St_Survey *) GetDataBase("Geometry/ssd/SsdLaddersOnSectors");
// wafers in the SSD ladder coordinate systems
St_Survey *SsdWafersOnLadders = (St_Survey *) GetDataBase("Geometry/ssd/SsdWafersOnLadders");
Local <-> Global transforms
A series of matrix multiplications

## Slide 14: Alignment methods (outline only)
There are ‘Global’ and ‘Self’ Alignment methods
  use ‘external’ track info or ‘internal’
We lack a hardware monitoring system. Once detectors are installed we rely on survey and alignment software
We have successful ‘Global’ methods already in place
  Software can be re-checked with simulations [->need (now have) geometry]. In SVT era precision was 10 microns and 0.1mrad
  In PXL era should practically vanish
  Specific alignment procedures might be different (next slide)
We now have significant sensor overlap to make use of ‘Self’ alignment methods. Industry standard is ‘Millepede’ code which was successfully used in Alice and elsewhere

## Slide 15: Procedure
TPC only tracks
  Global alignment of SSD (+SVT) with respect to TPC
  (Local) Alignment of SSD ladders:
TPC + SSD tracks
  (Global) Alignment of SVT Clam Shells
  (Local) Alignment of SVT ladders
TPC + SSD + SVT tracks
  Check consistency and
  re-evaluate SVT & SSD hit errors
Statistics needed:
1 mm  ~20 micron: reduction factor 50
~2,500 tracks per SVT sensor
data sample with ~250,000 tracks -> 250K CuCu events
PXL detector is a big asset (avoid TPC distortions):
Primary tracks with TPC+PXL hits
  Relative alignment of PXL halves (check survey)
  Alignment of IST ladders with respect to PXL
Primary tracks with (All – SSD) hits
  Alignment of SSD ladders
OLD ->
NEW ->

## Slide 16: Figure of merit for HFT alignment.
For alignment we use “good” (well defined) tracks fitted with the primary vertex.
  Use of primary tracks significantly improves precision of track predictions in Silicon detectors and reduces influence of systematics.
In order to minimize TPC space-charge distortions (and PXL pileup) we will need to use low luminosity data
Pointing accuracy, aka Impact parameter resolution:
  DCA resolution (in bending XY  plane: DCA), and resolution in non-bending plane: z, is figure of merit
  2DCA= 2vertex+ 2track + 2MCS (the same for non-bending plane),
  primary vertex resolution: vertex ~ 3mm+(120 mm / √Nch); for central Au+Au collisions turns out to be ~5 mm
  track pointing resolution: track ~ 1.5 XY in our case, where XY is intrinsic detector precision (~10mm)  alignment errors,
  Multiple Coulomb Scattering (MCS): MCS ~ 20mm / bp (GeV/c) (for thin PXL)
  Overall mis-alignments of < 10 mm are acceptable (no big impact)
Notes: Heavy d

## Slide 17: Schedule - Manpower
Some sub-system estimates are in following talks
We could use some more people here, especially a student ~50% at LBL
SSD, IST situation less clear

## Slide 18: Schedule
10/2011
10/2012
10/2013
NOW

## Slide 19: Open Items/Issues
Need to finalize the PXL sensor representation in Db. This will be done with the survey of the prototype sector
Need to setup Data formats, Db(s), code to deliver matrices
Need to clarify/verify/define reference system (physical) dependencies and hierarchy
Need to know/map the (realistic) error of every survey step
Need to start simulations to determine alignment software performance
Need to rework GEANT geometry synchronization (STV, VMC)
Need to finalize SSD procedures and initialize/define IST ones
Need to keep/use expertise around
Need to rework/prioritize Software Summer activities
See also sub-system specific issues

## Slide 20: Summary
Activity is picking up
Critical mass/think-tank is building
I do not see, or foresee, any show stoppers
but…most of the work is still ahead of us