## Slide 1
The Heavy Flavor Tracker (HFT) of STAR experiment and its PIXEL prototype beam tests
Spiros Margetis for the HFT group of the STAR experiment
Kent State University, USA
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
Notes: MAPS=Monolithic Active Pixel Sensor

## Slide 2: Talk Outline
The HFT (Heavy Flavor Tracker) detector in the STAR experiment at RHIC facility of BNL
HFT detector: physics goals, requirements, design and characteristics
PIXEL detector prototype beam tests
Summary.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 3: HFT Detector Motivation
Direct topological reconstruction of Charm
  Detect charm decays with small c, including D0  K 
Method: Resolve displaced vertices (50-100 microns)
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
We track inward from the TPC with graded resolution:
TPC
SSD
IST
PXL
~1mm
~300µm
~250µm
vertex
~30µm
Notes: Highlight detecting short lived particles –
you have heard about the physics in previous talks

## Slide 4: PXL Detector Requirements and Design Choices
-1 ≤ Eta ≤ 1, full Phi coverage (TPC coverage)
≤ 30 µm DCA pointing resolution required for 750 MeV/c kaon
  Two or more layers with a separation of > 5 cm.
  Pixel size of ≤ 30 µm
  Radiation length as low as possible but should be ≤ 0.5% / layer (including support structure). The goal is ~0.4% / layer
Integration time of < 200 μs
Sensor efficiency ≥ 99% with accidental rate ≤ 10-4.
Survive radiation environment.
Standard CMOS technology
Air cooling – room temperature operation
Thinned silicon sensors (50 μm thickness)
MAPS (Monolithic Active Pixel Sensor) pixel technology
  power dissipation ~170 mW/cm2 (integration time <200 μs) [digital output]
Quick extraction/replacement (1 day) with 20 mm envelope [4 copies]
Requirements
Design Choices
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
Notes: ATLAS ~ >2.5%
ALICE ~1-1.5%
L=8×1027

## Slide 5: Heavy Flavor Tracker (HFT)
TPC Volume
Magnet
Return Iron
Solenoid
EAST
WEST
FGT

## Slide 6: Heavy Flavor Tracker (HFT)
SSD
IST
PXL
HFT
Detector | Radius (cm) | Hit Resolution R/ - Z (m - m) | Radiation length
SSD | 22 | 20 / 740 | 1% X0
IST | 14 | 170 / 1800 | <1.5 %X0
PIXEL | 8 | 12/ 12 | ~0.4 %X0
 | 2.5 | 12 / 12 | ~0.4% X0
SSD
existing single layer detector, double side strips (electronic upgrade)
IST
one layer of silicon strips along beam direction, guiding tracks from the SSD through PIXEL detector. - proven strip technology
PIXEL
two layers
18.4x18.4 m pixel pitch
10 sector, delivering ultimate pointing resolution that allows for direct topological identification of charm.
new monolithic active pixel sensors (MAPS) technology

## Slide 7
PXL Detector Design
Carbon fibre sector tubes (~200µm thick)
Aluminum conductor Ladder Flex Cable
Ladder with 10 MAPS sensors (~ 2×2 cm each)
20 cm
The Ladders will be instrumented with sensors thinned down to 50 micron Si
Novel rapid insertion mechanism allows for dealing effectively with repairs.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
 coverage +-1
Inner layer
Outer layer
2.5 cm radius
8 cm radius
End view

## Slide 8
CD4
750 Kaon
THIN
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 9: Intermediate Silicon Tracker (IST)
Detail
24 ladders, liquid cooling.
Prototype Ladder
S:N > 20:1
>99.9% live and functioning channels
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 10: Silicon Strip Detector (SSD)
~ 1 Meter
44 cm
20 Ladders
Ladder Cards
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 11: Specific Engineering Goals for 2013 Run
Test PXL system (3/10 sectors) in beam conditions before deployment of full system
Integrate it with the STAR DAQ and Trigger system.
Explore many configurations/settings to optimize response and identify problems
Environment not optimal: p-p 500 GeV/c collisions at high luminosity
  Offline/reconstruction chain development/testing
  Calibration/Alignment code/procedures development/testing
  limited physics results expected from this sample
Most commissioning data are taken with the low-luminosity at STAR. De-steer beam to ~1-2% to reduce pile-up in TPC and PXL
Run finished just two weeks ago!
STAR HFT
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 12: Insertion into the experiment in May 2013
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
Actual size of PXL sectors as they are being mounted on the insertion mechanism

## Slide 13: Insertion into the experiment in May 2013
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
A PXL half holding two fully instrumented sectors (only the outer ladders can be seen) and three carbon (naked) sectors for smooth cooling. The other half had only one instrumented sector

## Slide 14: Insertion into the experiment in May 2013
Fabricated Assembled and tested at LBNL
Shipped to BNL
The PXL detector was assembled and tested in the STAR assembly area.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 15
PXL being pushed in and after installation in the East end of STAR
Insertion into the experiment in May 2013
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 16: Reducing Luminosity for suppressing Pileup event
~8kHz ZDC rate – 2% of full luminosity of p-p 500 GeV/c
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
The 0.2 ms readout makes the detector susceptible to non-triggered events (pileup)
Beams were displaced to reduce the effective luminosity by a factor of ~50
A special trigger was deployed to accept events where the event vertex was inside the useful acceptance of the detector. It also selected events with a total multiplicity above a certain threshold

## Slide 17: State of the Prototype - Example of QA plots
Several sensors were damaged during construction (red squares) and several were having hot pixels/column/rows (red dots and line)
A method to catalog and remove these noisy parts is being developed
Data will be used to address/correct issues in full system

## Slide 18: First look at Data
First tracking results shows matching of TPC tracks to hits on sensors with residual in order of the expected TPC resolutions on the sensors (~1-2 mm)
A beam (z) shift of ~3mm of the relative position of PXL and TPC is also observed
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 19: First look at Data
First look at alignment showed one sector (#4) being placed in almost ideal position and one (#7) deviating a few mm with some rotations
First pass corrections on sector #7 rectify some of the effect.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
BEFORE
AFTER

## Slide 20: Plans
We took a large data set of tracking data. ~ 6-10M events at end of fills (low luminosity runs).
We started systematic calibration/alignment studies
We are starting adding the Pxl information on tracks
We are starting looking into efficiency issues
The engineering run has been tremendously valuable and allow to identify problems, and will make next year’s startup smoother.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 21: IST mounting
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
The IST mounting on the MSC cone
Also the SSD will begin soon

## Slide 22
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 23
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 24: Summary
The HFT upgrade for STAR is in its final construction phase
The PXL detector will achieve a new standard in low radiation length vertex detectors
The prototype run of the heart of HFT, the PIXEL system, is a valuable step toward the success of the system and will insure quick physics results after each run
The final PXL detector along with the rest of the HFT upgrades will be installed for the November 2013 run.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 25
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
BACKUP SLIDES

## Slide 26: STAR Experiment
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
Notes: Highlight detecting short lived particles –
you have heard about the physics in previous talks

## Slide 27
PXL Detector Mechanical Design
Mechanical support with kinematic mounts (insertion side)
Insertion from one side
2 layers
5 sectors / half (10 sectors total)
4 ladders/sector
Aluminum conductor Ladder Flex Cable
Ladder with 10 MAPS sensors (~ 2×2 cm each)
carbon fiber sector tubes (~ 200 µm thick)
20 cm
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 28: HFT system
TPC – Time Projection Chamber
(main tracking detector in STAR)
HFT – Heavy Flavor Tracker
SSD – Silicon Strip Detector
  r = 22 cm
IST – Inner Silicon Tracker
  r = 14 cm
PXL – Pixel Detector
  r = 2.5, 8 cm
We track inward from the TPC with graded resolution:
TPC
SSD
IST
PXL
~1mm
~300µm
~250µm
vertex
~30µm
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
Notes: Ist is a silicon pad detector upgrade is several detectors, focus is on the pixle detectors. Other detectors connect tpc tracks with the pxl detector – don’t go into pointing

## Slide 29: Detector Characteristics
Pointing resolution | (12  19 GeV/pc) m
Layers | Layer 1 at 2.5 cm radius Layer 2 at 8 cm radius
Pixel size | 20.7 m X 20.7 m
Hit resolution | 6 m
Position stability | 6 m rms (20 m envelope)
Radiation length per layer | X/X0 = 0.37%
Number of pixels | 356 M
Integration time (affects pileup) | 185.6 s
Radiation environment | 20 to 90 kRad 2*1011 to 1012 1MeV n eq/cm2
Rapid detector replacement | ~ 1 day
356 M pixels on ~0.16 m2 of Silicon
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 30: Monolithic Active Pixel Sensors
Standard commercial CMOS technology
Room temperature operation
Sensor and signal processing are integrated in the same silicon wafer
Signal is created in the low-doped epitaxial layer (typically ~10-15 μm) → MIP signal is limited to <1000 electrons
Charge collection is mainly through thermal diffusion (~100 ns), reflective boundaries at p-well and substrate.
100% fill-factor
Fast readout
Digital output
Proven thinning to 50 micron
MAPS pixel cross-section (not to scale)‏
4um
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 31: Pixel signal extraction and operation
Capacitor Storage for Correlated Double Sampling (CDS)
 ~ 100 ms
Discriminator
Zero suppression and memory
LVDS outputs 160 MHz
1
2
3
(Sample 1 – Sample 2) > threshold => hit
(Sample 2 – Sample 3) < threshold => no hit
CDS
Simplified description
O
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 32: Final PXL sensor design
  Based on Mimosa-26 architecture
  Reticle size (~ 4 cm²)
    Pixel pitch 20.7 μm
    928 x 960 array ~890 k pixels
  Reduced power dissipation
    Vdd: 3.0 V
    Estimated power dissipation ~134 mW/cm²
  Short integration time 185.6 μs
  on-chip zero suppression
  2 LVDS data outputs @ 160 MHz
  High Res Si option – significantly increases S/N and radiation tolerance.
The final PXL sensor is an extension of development work already done at IPHC and is based on the Mimosa-26 sensor currently used in the EUDET detector telescope.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
Notes: This is the sensor design for the final detector

## Slide 33: Mimosa-26HR eff vs. fake hit rate
Tested for STAR Operating conditions
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
Notes: Summarize advantages – greater signal to noise, etc. this gives a comfortable margin in performance

## Slide 34: Mimosa-26 in HR
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 35: PXL detector production prototype
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 36: HFT PXL– fabrication and tooling
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 37: Mechanical Development
Silicon power: tested at 170 mW/cm2 (~ power of sunlight)
350 W total in the ladder region (Si + drivers)
computational fluid dynamics
Air-flow based cooling system for PXL to minimize material budget.
Detector mockup to study cooling efficiency
ladder region
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013
Notes: Explain problem and then go into details.

## Slide 38: Mechanical Development
Power ~340 W Airflow 10.1 m/s
Thermal camera image of sector 1 (composite image):
unsuported end
mid-section
fixed end
Solid – inner layer
Open – outer layer
340 W with ambient air = 26.8 C
NTC thermistors
(averaged at same “Z” position)
Measurement results agree with simulations and meets calculated stability envelope tolerance.
Air flow-induced vibrations (≤ 10 m/s) are within required stability window.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013

## Slide 39: Fast, column-parallel architecture
CDS at column level (reduces Fixed Pattern Noise below temporal noise)
VREAD,CALIB
VC
Vin1,2
VS_READ
A1 Voff1
A2, Voff2
Developed in IPHC - DAPNIA collaboration
Notes: The sensor architecture presented in this diagram has been developed and tested in the collaboration between IPHC and DAPNIA.
This architecture is suitable for building fast detectors thanks to a collumn parallel readout and on-chip signal processing.
Each pixel contains an amplifier and a circuit preforming Correlated-Double-Sampling. An in pixel amplifier is a critical component that allows to improve signal-to-noise ratio that is crucial for on-chip signal processing.
The circuitry at the bottom is an offset-compensated discriminator.
The timing diagram presented here and these simple equations show how this circuit operates. Let me poitn out that correlated double sampling is basically performed twice:
inside a pixel it allows for signal extraction,
at the column level – it reduces pixel-to-pixel dispersions by cancelling the incluence of the source follwer threshold variations.
This allows reducing the fixed patter noise below the temporal noise level.

## Slide 40: CD-4 performance parameters
1 | Thickness of first PXL layer | < 0.6% X0 (0.37% in the baseline design) | Measured during construction
2 | Internal alignment and stability PXL | < 30 m (This requirement is met in the baseline mechanical design, verified by simulation and prototype testing) | Measure during prototype testing and with test beam or cosmic rays after construction.
4 | PXL integration time | < 200 s (Current generation sensors have an integration time of 185.6 s) | This is a design parameter of the sensor. This can be demonstrated with oscilloscope measurements.
5 | Detector hit efficiency PXL | 95% sensor efficiency and noise from all sources < 10-4 (Prototype sensors measured in beam tests to be > 99% with noise < 10-4) | The sensor efficiency will be measured in beam tests as a function of bias settings and threshold. This will be established prior to construction.
7 | Live channels for PXL and IST | 95% (The measured good sensor live channel yield fraction is > 99% for over 90% of sensors on a wafer. We will select good sensors for production ladders) | The number of bad pixels will be measured on each mounted sensor during probe testing and verified after ladder and sector construction. The numbers will be saved to a database.
8 | PXL and IST Readout speed and dead time | <5% additional dead time @ 500 Hz average trigger rate and simulated occupancy | This can be measured in real time with simulated data for verification.
Low-level CD-4 key performance parameters: experimentally demonstrated at Project Completion
Our current design meets (and exceeds) these requirements.
The 2013 International Conference on Applications of Nuclear Techniques Crete, Greece June 23-29, 2013