## Slide 1: Geometry update
Estimation of material budget for geometry dev13 [AgML]
  Dev13 has the IDSM = PXL + FGT
  Use of Jason Webb’s code [StarBASE] to plot radiation length vs η,φ :
    η,φ ranges and binning , as well as the number of triggers per bins can be set up : more handy than the starsim command
    It plots the radiation length for a given GEANT volume, not by choosing the [Rmin,Rmax] range from the Starsim command
Update on MSC geometry :
  Implementation of the inner ring support of the PST
  Initial version of the PIT
Input for SST+IST simulation

## Slide 2: Radiation length vs η for IDSM, PIXEL, FGT
Default parameters are :
  Ntrig = 4
  dφ =.2
  dη = .1
  |η|<6
  |φ|<1 deg.
same with Ntrig =100
increasing the # of triggers give a slightly better resolution
(see comparison for the FGT at
slide 10)

## Slide 3: PIXEL
Only the active silicon ladder and sector support using a carbon Fiber mixture [taken from the FGT code] is implemented . This may not represent the final version since it misses the sensors cables/electronics and maybe a more accurate of the sector material
Black = all pixel material
Red = only silicon active material

## Slide 4: Comparison with calculation/expectation
✔numbers agree (pretty well for the active silicon) with the plots
For the black line (which is all the material) , remember that we don’t have in AgML ALL the material and that the support structure have a carbon fiber mix that may not reflect the reality ( I took the mixture definition from the FGT)
from Spiros/Flemming numbers, per ladder :
Radiation length of the active silicon is 0.0677% X0
Radiation length of the Total (silicon+cables+backer+support beam) is 0.3688%
For 2 ladders (inner and outer), this makes :
Active silicon = 0.1354% X0
Total = 0.7376% X0

## Slide 5: Radiation length vs. η and φ
Left : rad. Len. vs. η
Right : rad Len distribution integrated over η
Left : rad. Len. vs. φ
Right : rad Len distribution integrated over φ
we see peaks (10) due to the 10 sectors (tracks crossing the entire support)
We also see small peaks denoting overlaps between ladders

## Slide 6: Pixel Support Tube
The inner rings supports have been simplified
Reason : I don’t know how to represent this piece, it has no symmetry

## Slide 7: MSC = PIT + PST
Pixel Support Tube
Pixel Insertion Tube

## Slide 8
subsystem | Geometry [UPGR15] | Geometry [dev13] | BFC tracking in UPGR15 | BFC tracking in DEV13
SSD | yes | yes | yes | Did not try yet
IST | yes | no | yes | X
PIXL | yes | 75% | yes | no
Geometry UPGR15 :
SSD fully described
PXL and IST are approximated by cylinders
Geometry DEV13 :
SSD fully described
PXL modelized according SolidWorks, no IST in AgML

## Slide 9: summary
Material length study :
  code to evaluate is pretty accurate and flexible
  Material budget of the pixel is agree with WHAT we have implemented so far
Geometry model of DEV13 :
  Implementation of inner rings support
  Need to know the level of precision we need ?
  PIT implemented
To do :
  Evaluate material distribution of MSC
  Long time issue : tracking with AgML not working with Pixel hits

## Slide 10: comparison
Ntrig=40
Ntrig=100

## Slide 11
Si 2 mil (0.0529%)
acrylic 2 mil (0.0148%)
sensor
cable
backer
support
beam
acrylic 2 mil (0.0148%)
acrylic 2 mil (0.0148%)
Al 0.7 mil (0.0124%)
kapton 1mil (0.0073%)
Al 0.7 mil (0.0124%)
Al 0.7 mil (0.0124%)
kapton 1mil (0.0073%)
Al 0.7 mil (0.0124%)
10 mil carbon composite
open weave (0.0587%)
4 mil silicon adhesive
(0.0469%)
9.6 mil carbon composite
sector beam (0.1017%)
0.0677%
0.079%
0.223 mm
0.2221%
TOTAL = 0.3688 % X0
Notes: Curtsey Leo

## Slide 12: Check with the [SSD] volume
ALL “SSD”
SSD LADDERS
RDO
ACTIVE SILICON
Vs. eta
Vs. radius
Vs. z